National Aeronautics and

Space Administration

Student Launch Initiative

Preliminary Design Review

1 Summary of PDR report

1.1 Team summary

1 Cheyenne Mountain Charter Academy

2 The Vanguard School

1605 S. Corona Avenue

Colorado Springs, Colorado 80905

3 Mentors: Jeff Lane, Ernie Puckett, Steve Madere, Warren Layfield, George Schaffer, Jason Unwin, Ann Conner

1.2 Launch Vehicle Summary

1. Size: 95 inches long x 3.9 inches in diameter

2. Motor choice: Animal Motor Works (AMW) K350RR High Power Rocket Motor

3. Recovery system: Main Parachute bay 18 inches long [100in round main parachute].   Drogue Parachute Bay 14 inches long [30in round drogue parachute]

1.3 Payload Summary

1. We will place a digital camera and GPS in the rocket and a known-length object on the ground, and then we will be able to determine the exact level of accuracy of the altimeter through comparison of GPS data, pixel analysis, and altimeter data.

1.b Data analysis issues:

While the altimeter is more precise than the camera, the velocity of the rocket flops this relationship because of the sample rate (ten per second) of the altimeter.

If the rocket accelerates to 150fps at the end of the 8 foot launch rail in .15 sec (general numbers from Rocksim), we'll have one data point from the altimeter and 9 frames from the camera (at 60 fps) by the time the rocket leaves the rail.

The lower the camera is (the closer to the measuring device), the more precise it is. Though we won't need to do this, with the camera closer to the ground, and with its resolution capabilities, we could determine altitude down to a fraction of an inch if we had a regular ruler on the ground for the camera to shoot. The altimeters are not capable of this level of precision.

Therefore, at a specific distance from the measuring device (very generally this distance is probably one pixel per foot in each frame), the camera's digital pixels become LESS precise than the altimeter's output, given a static altitude. This distance would be 1280 feet in altitude (1280 pixels of resolution) with a normal lens.

The rocket's velocity will peak just before motor burnout at around 2.5 seconds. Coincidentally, this will occur at about the same altitude that our camera becomes less precise than our altimeter, but with a velocity of around 800 fps, we'll be getting data points every 80 feet from the altimeter, whereas we'll still be getting digital frames every 13 feet from the camera (at 60fps). When we add velocity into the big picture, the tipping point (with a normal lens at 60fps) will be where the velocity slows to significantly less than 100fps and the altitude is well above 5000 ft.

The camera is being used in the experiment as the reference device; precision is based on repeatable and reliable static tests on the ground to obtain a “true” and valid altitude. Our hypothesis is that the altimeters are not accurate, because our experience with them is that they're not, and each altimeter's accuracy varies at different altitudes when comparing multiple altimeters.

The repeatable nature of data points from the altimeters is not a consideration in our experiment. Additional experimentation might be done in the future to establish how far they deviate from one flight to another.

Data will be collected and compared after the flight, not live. Because of the lag for air escaping from the payload bay, and because the barometric altimeters don’t begin recording until 40-250 to reduce false triggering from wind gusts, we will have significant work post-flight synchronizing the video data with the altimeter data.

2 Changes Made Since Proposal

1. We have made no changes to our vehicle criteria, payload criteria, or activity plan so far.

3 Vehicle Criteria

3.1 Selection, Design, and Verification Launch Vehicle

1. Our mission is to build, test, fly, and recover a reusable rocket with a scientific payload with altimeters and cameras and to gather data to test the accuracy of the altimeters. As a secondary mission, we hope to inspire teenagers to consider careers as scientists and engineers.

2. If our mission is successful we shall be able to create a smooth, precise curve on a chart and compare with the data from the various altimeters to determine the altimeters’ accuracy.

3.5. We are concerned about breaking a material while testing it, therefore we will take necessary precautions to be careful with our tests.

We are concerned about parts not arriving on time, so we will order each part before needed in case of setbacks.

We are concerned about not having enough people to test the materials and test fly the rocket, so we have made sure that each person on the team is eligible to fly rockets and test them.

We have encouraged commitment to this program by requiring a monthly fee of 100 dollars from each family with scholarships available for those who qualify for federal school lunch programs.

School holidays have proven to be a problem because many of our members go on vacations and therefore do not attend meetings and tests. To stop this from happening we either cancel the meeting so they don’t miss any vital information or tests or have another meeting.

3.6. We will test the body tube with deformation tests. We will do deformation tests on the nose cone. We will also do flex test on the fins. We will also test all joints and anchor points to be sure of strength. In addition, we will get as much materials stress test information on each component from the manufacturers as possible.

4. Recovery Subsystem.

4.1 Using uroc.org design tools we have determined that we need a main parachute diameter of 105.06, drogue parachute diameter of 31.52 inch, and 2 grams of black powder for the main ejection charge and 1.34 grams for the drogue.

5. Mission performance

5.1 For our mission to be a success we must be able to fly and recover the rocket, gather the data, and compare it to determine how accurate altimeters are.

6.Payload integration

6.1 We have three separate payload bays in our rocket. The first one consists of the GPS unit and is located at the very front of the rocket right below the nosecone. The next bay is the camera bay and it is located below the GPS bay. On the outside of the rocket is a hole where light enters the camera lens. Against the hole is a small mirror placed at a 45 degree angle so the camera can look down the side of the rocket towards the ground. On top of the mirror is a hood that protects the mirror and creates a better aerodynamic design with lower drag coefficient and less asymmetry to change the path of the rocket. The last payload bay is the altimeter bay. This houses the altimeters which eject the parachutes and collect the data.

7. Launch operation procedures

7.1 We will be using a custom made launch system fabricated by Ernie Puckett and a custom made launch pad made by Norman Pfund with a ¼ inch 8 foot long launch rail.

8. Safety and Environment

8.1 Our team’s safety officer is Trenton Tulloss.

8.2			 Safe Distances

-No person shall be closer to the launch of a high power rocket than the person actually launching the rocket and those authorized by the Safety Monitor (Trenton).

-All spectators shall remain within an area determined by the Safety Monitor and behind both the Safety Monitor and the person launching the rocket.

-A person shall not be closer to the launch of a high power rocket than the applicable minimum safe distance.

- Launch Operations

-Do not ignite and launch a high power rocket horizontally, at a target, in such a way that the rocket's flight path goes into clouds or beyond the boundaries of the flying field (launch site).

-Do not launch a high power rocket if the surface wind at the launch site is more than twenty (20) miles per hour.

-Do not operate a high power rocket in a manner that is hazardous to aircraft.

- Launch Control.

-Launch a high power rocket only with the immediate knowledge, permission, and attention of the Safety Monitor.

-All persons involved in the launch, all spectators, and parking areas during a countdown and launch shall be facing the launcher if requested to do so by the Safety Monitor.

-Precede the launch with a five (5) second countdown audible throughout the launching, spectator, and parking areas. This countdown shall be given by the person launching the rocket, the Safety Monitor, or other launch site operating personnel.

-Do not approach a high power rocket that has misfired until the safety inter-lock has been removed or the battery has been disconnected from the ignition system, one minute has passed, and the Safety Monitor has given permission for only a single person to approach the misfired rocket to inspect it.

Safety Tables

TABLE 1: LAUNCH SITE DIMENSIONS

| Installed Total Impulse (N-sec) | Equivalent Motor Type | Minimum Site Distance (feet) | Equivalent Distance (miles) |
| --- | --- | --- | --- |
| 160.01 - 320.00 | H | 1,500 | .28 |
| 320.01 - 640.00 | I | 2,500 | .50 |
| 640.01 - 1280.00 | J | 5,280 | 1.00 |
| 1280.01 - 2560.00 | K | 5,280 | 1.00 |
| 2560.01 - 5120.00 | L | 10,560 | 2.00 |
| 5120.01 - 10240.00 | M | 15,480 | 3.00 |
| 10240.01 - 20480.00 | N | 21,120 | 4.00 |
| 20480.01 - 40960.00 | O | 26,400 | 5.00 |

TABLE 2: SAFE DISTANCE

| Installed Total Impulse (N-sec) | Equivalent Motor Type | Minimum Safe Distance (feet) | Complex Minimum Safe Distance (feet) |
| --- | --- | --- | --- |
| 160.01 - 320.00 | H | 50 | 100 |
| 320.01 - 640.00 | I | 100 | 200 |
| 640.01 - 1280.00 | J | 100 | 200 |
| 1280.01 - 2560.00 | K | 200 | 300 |
| 2560.01 - 5120.00 | L | 300 | 500 |
| 5120.01 - 10240.00 | M | 500 | 1,000 |
| 10240.01 - 20480.00 | N | 1,000 | 1,500 |
| 20480.01 - 40960.00 | O | 1,500 | 2,000 |

MATERIAL SAFETY DATA SHEET

1. CHEMICAL PRODUCT AND COMPANY IDENTIFICATION

| Elmer's Products, Inc. | Emergency Phone Number: |
| --- | --- |
| 1 Easton Oval | Poison Control Center |
| Columbus, OH 43219 | 1-888-516-2502 |

For additional product information, access our website at www.elmers.com or call 1-888-435-6377. To place an order, call 1-800-848-9400. 

SUBSTANCE: ELMER'S ULTIMATE GLUE

TRADE NAMES/SYNONYMS:
P9405; P9406; P9411; P9412; P9413; P9415; P9416; P9417

CREATION DATE: Jun 08 2007
REVISION DATE: Jun 22 2007

2. COMPOSITION, INFORMATION ON INGREDIENTS

COMPONENT: POLYMETHYLENE POLYPHENYL ISOCYANATE
CAS NUMBER: 9016-87-9
PERCENTAGE: 30-50

COMPONENT: METHYLENE BISPHENYL ISOCYANATE
CAS NUMBER: 101-68-8
PERCENTAGE: 30-50

COMPONENT: NON-HAZARDOUS SUBSTANCE
CAS NUMBER: Not assigned.
PERCENTAGE: 10-30

COMPONENT: CHLOROBENZENE
CAS NUMBER: 108-90-7
PERCENTAGE: <0.01

3. HAZARDS IDENTIFICATION

NFPA RATINGS (SCALE 0-4):  HEALTH=2 FIRE=1  REACTIVITY=1

EMERGENCY OVERVIEW:
COLOR: brown
PHYSICAL FORM: liquid
ODOR: musty odor
MAJOR HEALTH HAZARDS: harmful if inhaled, respiratory tract irritation, skin irritation, eye irritation, allergic reactions
PHYSICAL HAZARDS: May react on contact with water.

POTENTIAL HEALTH EFFECTS:
INHALATION:
SHORT TERM EXPOSURE: irritation, allergic reactions, chest pain, difficulty breathing
LONG TERM EXPOSURE: allergic reactions, difficulty breathing
SKIN CONTACT:
SHORT TERM EXPOSURE: irritation, allergic reactions, skin disorders, itching, rash
LONG TERM EXPOSURE: irritation, allergic reactions, rash, itching
EYE CONTACT:
SHORT TERM EXPOSURE: irritation
LONG TERM EXPOSURE: irritation
INGESTION:
SHORT TERM EXPOSURE: gastrointestinal irritation
LONG TERM EXPOSURE: no information on significant adverse effects

4. FIRST AID MEASURES

INHALATION: If adverse effects occur, remove to uncontaminated area. Give artificial respiration if not breathing. If breathing is difficult, oxygen should be administered by qualified personnel. Get immediate medical attention.

SKIN CONTACT: If bonding occurs, immerse the bonded surfaces in warm soapy water. Peel or roll the surfaces apart using a blunt edge, such as a spatula or spoon handle. Do not pull surfaces apart with a direct opposing action. If burns occur, treat as thermal burns. Get medical attention, if needed.

EYE CONTACT: If bonding to tissues occurs, wash with large amounts of warm water. Cover both eyes with sterile, dry bandages. The eye will open without further action. Do not pull surfaces apart with a direct opposing action. If burns occur, treat as thermal burns. Get medical attention.

INGESTION: Wet lips with water. Peel or roll the surfaces apart using a blunt edge, such as a spatula or spoon handle. Do not pull surfaces apart with a direct opposing action. If a lump forms in the mouth, turn head to side. If burns occur, treat as thermal burns. Get medical attention.

NOTE TO PHYSICIAN: For inhalation, consider oxygen. Mineral oil, vegetable oil, or petroleum jelly may help soften the bonding between skin surfaces. For skin contact, consider acetone or nitro methane.

5. FIRE FIGHTING MEASURES

FIRE AND EXPLOSION HAZARDS: Slight fire hazard.

EXTINGUISHING MEDIA: carbon dioxide, regular dry chemical, regular foam, water

FIRE FIGHTING: Move container from fire area if it can be done without risk. Avoid inhalation of material or combustion by-products. Stay upwind and keep out of low areas.

FLASH POINT: >230 F (>110 C) (CC)
AUTOIGNITION: >1112 F (>600 C)
FLAMMABILITY CLASS (OSHA): IIIB

HAZARDOUS COMBUSTION PRODUCTS:
Thermal decomposition or combustion products: cyanides, oxides of carbon, oxides of nitrogen

6. ACCIDENTAL RELEASE MEASURES

OCCUPATIONAL RELEASE:
Stop leak if possible without personal risk. Small spills: Absorb with sand or other non-combustible material. Collect spilled material in appropriate container for disposal. Notify Local Emergency Planning Committee and State Emergency Response Commission for release greater than or equal to RQ (U.S. SARA Section 304). If release occurs in the U.S. and is reportable under CERCLA Section 103, notify the National Response Center at (800)424-8802 (USA) or (202)426-2675 (USA).

7. HANDLING AND STORAGE

STORAGE: Store and handle in accordance with all current regulations and standards. Keep container tightly closed. Store in a well-ventilated area. Avoid contact with water or moisture. Store between 16 C and 38 C. A hazardous build-up of pressure could result due to a reaction with water producing carbon dioxide gas if contaminated containers are resealed. Do not reseal contaminated containers. Reseal uncontaminated containers that are free of moisture only after placing under a nitrogen blanket. Do not store in containers made of copper, copper alloys, or galvanized surfaces. See original container for storage recommendations. Keep separated from incompatible substances.

HANDLING: Use only with adequate ventilation. Avoid breathing vapor or mist. Avoid prolonged or repeated contact with skin or eyes. Wash thoroughly after handling. Do not get in eyes.

8. EXPOSURE CONTROLS, PERSONAL PROTECTION

EXPOSURE LIMITS:
POLYMETHYLENE POLYPHENYL ISOCYANATE:
METHYLENE BISPHENYL ISOCYANATE:
0.02 ppm (0.2 mg/m3) OSHA ceiling
0.005 ppm ACGIH TWA
0.005 ppm (0.05 mg/m3) NIOSH recommended TWA 10 hour(s)
0.020 ppm (0.2 mg/m3) NIOSH recommended ceiling 10 minute(s)

METHYLENE BISPHENYL ISOCYANATE:
0.02 ppm (0.2 mg/m3) OSHA ceiling
0.005 ppm ACGIH TWA
0.005 ppm (0.05 mg/m3) NIOSH recommended TWA 10 hour(s)
0.020 ppm (0.2 mg/m3) NIOSH recommended ceiling 10 minute(s)

VENTILATION: Provide local exhaust or process enclosure ventilation system. Ensure compliance with applicable exposure limits.

EYE PROTECTION: Wear splash resistant safety goggles with a face shield. Provide an emergency eye wash fountain and quick drench shower in the immediate work area.

CLOTHING: Wear appropriate chemical resistant clothing.

GLOVES: Wear appropriate chemical resistant gloves.

PROTECTIVE MATERIAL TYPES: neoprene, nitrile, butyl rubber

RESPIRATOR: Under conditions of frequent use or heavy exposure, respiratory protection may be needed. Respiratory protection is ranked in order from minimum to maximum. Consider warning properties before use.
Any dust, mist, and fume respirator.
Any air-purifying respirator with a high-efficiency particulate filter.
Any powered, air-purifying respirator with a dust, mist, and fume filter.
Any powered, air-purifying respirator with a high-efficiency particulate filter.
For Unknown Concentrations or Immediately Dangerous to Life or Health -
Any supplied-air respirator with full face piece and operated in a pressure-demand or other positive-pressure mode in combination with a separate escape supply.
Any self-contained breathing apparatus with a full face piece.

9. PHYSICAL AND CHEMICAL PROPERTIES

PHYSICAL STATE: liquid
COLOR: brown
ODOR: musty odor
BOILING POINT: >572 F (>300 C) (decomposes)
FREEZING POINT: Not available
VAPOR PRESSURE: 0.000004 mmHg
VAPOR DENSITY (air=1): 8.5
SPECIFIC GRAVITY (water=1): 1.129
WATER SOLUBILITY: reacts, immiscible
PH: Not available
VOLATILITY: Not available
ODOR THRESHOLD: Not available
EVAPORATION RATE: Not available
VISCOSITY: 2311 cP
COEFFICIENT OF WATER/OIL DISTRIBUTION: Not available

10. STABILITY AND REACTIVITY

REACTIVITY: May react on contact with water. Closed containers may rupture.

CONDITIONS TO AVOID: Avoid heat, flames, sparks and other sources of ignition. Avoid contact with incompatible materials.

INCOMPATIBILITIES: acids, alcohols, amines, bases, combustible materials, metal salts, metals, oxidizing materials

HAZARDOUS DECOMPOSITION:
Decomposition products on contact with water or moisture: oxides of carbon
Thermal decomposition or combustion products: cyanides, oxides of carbon, oxides of nitrogen

POLYMERIZATION: Polymerization may occur in the presence of metal compounds, alkalies, and tertiary amines at elevated temperatures.

11. TOXICOLOGICAL INFORMATION

ELMER'S ULTIMATE GLUE:
MEDICAL CONDITIONS AGGRAVATED BY EXPOSURE: skin disorders, respiratory system (including asthma and other breathing disorders)

POLYMETHYLENE POLYPHENYL ISOCYANATE:
IRRITATION DATA: 100 mg eyes-rabbit mild
TOXICITY DATA: 490 mg/m3/4 hour(s) inhalation-rat LC50; >5 ml/kg skin-rabbit LD50; >10000 mg/kg oral-rat LD50
CARCINOGEN STATUS: IARC: Human No Adequate Data, Animal No Adequate Data, Group 3
LOCAL EFFECTS:
Irritant: inhalation, skin, eye
ACUTE TOXICITY LEVEL:
Highly Toxic: inhalation
Relatively Non-toxic: ingestion
TARGET ORGANS: immune system (sensitizer)
TUMORIGENIC DATA: Available.
REPRODUCTIVE EFFECTS DATA: Available.
ADDITIONAL DATA: May cross react with similar compounds.

METHYLENE BISPHENYL ISOCYANATE:
IRRITATION DATA: 500 mg/24 hour(s) skin-rabbit; 100 mg eyes-rabbit moderate
TOXICITY DATA: 178 mg/m3 inhalation-rat LC50; 9200 mg/kg oral-rat LD50
CARCINOGEN STATUS: IARC: Human Inadequate Evidence (Monomer), Group 3
LOCAL EFFECTS:
Irritant: inhalation, skin, eye
ACUTE TOXICITY LEVEL:
Highly Toxic: inhalation
Slightly Toxic: ingestion
TARGET ORGANS: immune system (sensitizer)
MEDICAL CONDITIONS AGGRAVATED BY EXPOSURE: respiratory disorders
MUTAGENIC DATA: Available.
REPRODUCTIVE EFFECTS DATA: Available.

12. ECOLOGICAL INFORMATION

Not available

13. DISPOSAL CONSIDERATIONS

Dispose in accordance with all applicable regulations.

14. TRANSPORT INFORMATION

U.S. DEPARTMENT OF TRANSPORTATION: No classification assigned.

CANADIAN TRANSPORTATION OF DANGEROUS GOODS: No classification assigned.

15. REGULATORY INFORMATION

U.S. REGULATIONS:
CERCLA SECTIONS 102a/103 HAZARDOUS SUBSTANCES (40 CFR 302.4): 
METHYLENE BISPHENYL ISOCYANATE: 5000 LBS RQ
CHLOROBENZENE: 100 LBS RQ

SARA TITLE III SECTION 302 EXTREMELY HAZARDOUS SUBSTANCES (40 CFR 355.30): Not regulated.

SARA TITLE III SECTION 304 EXTREMELY HAZARDOUS SUBSTANCES (40 CFR 355.40): Not regulated.

SARA TITLE III SARA SECTIONS 311/312 HAZARDOUS CATEGORIES (40 CFR 370.21): 
ACUTE: Yes
CHRONIC: Yes
FIRE: No
REACTIVE: No
SUDDEN RELEASE: No

SARA TITLE III SECTION 313 (40 CFR 372.65): 
POLYMETHYLENE POLYPHENYL ISOCYANATE
METHYLENE BISPHENYL ISOCYANATE

OSHA PROCESS SAFETY (29CFR1910.119): Not regulated.

STATE REGULATIONS:
California Proposition 65: Not regulated.

CANADIAN REGULATIONS:
WHMIS CLASSIFICATION: Not determined.

NATIONAL INVENTORY STATUS:
U.S. INVENTORY (TSCA): All the components of this substance are listed on or are exempt from the inventory.

TSCA 12(b) EXPORT NOTIFICATION: 
CHLOROBENZENE
CAS NUMBER: 108-90-7
SECTION 4

CANADA INVENTORY (DSL/NDSL): Not determined.

16. OTHER INFORMATION

©Copyright 1984-2007 MDL Information Systems, Inc. All rights reserved.

SELLER MAKES NO WARRANTY, EXPRESS OR IMPLIED, CONCERNING THE PRODUCT OR THE MERCHANTABILITY OR FITNESS THEREOF FOR ANY PURPOSE, except that the product shall conform to contracted specifications, and that the product does not infringe any valid United States or Canadian patent. No claim of any kind shall be greater in amount than the purchase price of the quantity of product in respect of which damages are claimed. In no event shall Seller be liable for incidental or consequential damages, whether Buyer's claim is based on contract, breach of warranty, negligence or otherwise.

MATERIAL SAFETY DATA SHEET

02/20/08

Revision #7

Section 1 HAZARD RATING For Chemical Emergency Only:

PACER TECHNOLOGY In the US & Canada (800) 424-9300

9420 Santa Anita Avenue 2 Int'l & Wash DC (COLLECT) (703) 527-3887

Rancho Cucamonga, CA 91730 1 x 1 Telephone for Information :(909) 987-0550

PRODUCT IDENTIFICATION: Super Glue Gel

Section 2 - HAZARDOUS INGREDIENTS INFORMATION:

Hazardous Components OSHA ACGIH OTHER %

(Common Names, CAS Number) PEL TLV LIMITS OPTION

Ethyl-2-Cyanoacrylate (7085-85-0) NE NE 0.2ppm TWA 60-100

Poly (Methyl Methacrylate) (9011-14-7) NE NE 10-30

Hydroquinone* (123-31-9) 2mg/m3 2mg/m3 0-1

*This ingredient is subject to the reporting requirements of Section 313 of Title III of the Superfund

Amendments & Reauthorization Act of 1986 (SARA) and 40 CFR 372.

Section 3 - PHYSICAL/CHEMICAL CHARACTERISTICS:

Boiling Point: 365 F Specific Gravity (H2O=1): 1.05

Vapor Density (Air=1): nil-NE Melting Point: NE

Vapor Pressure (mm Hg): 1 @ 20 C Evaporation Rate (Butyl acetate=1): nil-NE

Solubility in Water: Insoluble, material reacts to hardened mass for non-hazardous waste.

VOC: This product is VOC compliant for sale in California.

Appearance & Odor: Transparent water-white to straw colored liquid with stimulative odor.

Section 4 - FIRE AND EXPLOSION HAZARD DATA:

Flash Point (Method Used): 185 F (TCC) Flammable Limits: LEL: NE UEL: NE

Extinguishing Media: Flush with large amounts of water or dry chemical extinguisher.

Special Fire Fighting Procedures: Fumes may be irritating if not burning and require air supply with goggles while applying large amounts of water or dry chemical extinguisher.

Unusual Fire and Explosion Hazards: None. Combustible requiring the above procedures.

Section 5 - REACTIVITY DATA:

Stability: Stable XX Conditions to Avoid: Excessive heat above 176 F, moisture and alkaline. Stable up to 122 F. Store in a cool dry place.

Incompatibility (Materials to Avoid): Polymerized by water, alcohol, amines, alkaline materials and direct UV.

Hazardous Decomposition Products: Combustible by-products of carbon monoxide/dioxide.

Hazardous Polymerization: May Not Occur XX

Section 6 - HEALTH HAZARD DATA:

Route(s) of Entry: Inhalation: Yes Skin: NO Ingestion: LD50 = 12.2cc/kg

Health Hazards (Acute and Chronic): (mice)

Acute - Irritates eyes, mucous membranes.

Chronic - No residual effects of acute properties.

MATERIAL SAFETY DATA SHEET Super Glue Gel Revision #7 Page 2 of 2

Carcinogenicity: NTP: No IARC Monographs: No OSHA Regulated: No

First Aid Procedures:

Eye contact - Tearing from eye irritation. Remove to fresh air. Flush areas of contact with water.

Adhesive will disassociate from eye/eyelids over time, usually within several hours. Temporary weeping of eyes/double vision may be experienced until clearance is achieved.

Skin contact - Immerse bonded areas in warm, soapy water. Peel or roll skin apart. Remove cured adhesive with several applications of warm, soapy water. Prolonged or repeated contact at elevated levels may cause dermatitis in sensitive individuals.

Inhalation - Irritation of mucous membranes/coughing. Remove to fresh air. Prolonged or repeated exposure at elevated levels may produce allergic reactions with asthma-like symptoms in sensitive individuals.

Ingestion - Lips may become stuck together: apply copious amounts of warm water & encourage wetting/pressure from saliva inside mouth. Peel or roll (do not pull) lips apart. It is almost impossible to swallow cyanoacrylate as adhesive solidifies upon contact with saliva & may adhere to inside of mouth. Saliva will lift adhesive in 1-2 days, avoid swallowing adhesive after detachment.

Medical Conditions Generally Aggravated by Exposure: Pre-existing skin, eye and respiratory disorders may be aggravated by exposure.

Section 7 - PRECAUTIONS FOR SAFE HANDLING AND USE:

Steps to be taken in Case Material is Released or Spilled: Polymerize with water. Solid material may be scraped from surface.

Waste Disposal Method: Incinerate solid combustible waste or dump as chemical waste according to local, state and federal regulations.

Precautions to Be Taken in Handling and Storing: Avoid contact with clothing as contact can cause burn. Avoid moisture, direct UV-sunlight and do not store above 25 C. Keep containers closed tightly when not in use. Ideal storage: 5-10 C.

Other Precautions: Avoid breathing vapor, contact with eyes/skin. Allow product to reach room temperature before use.

Section 8 - CONTROL MEASURES:

Respiratory Protection (Specify Type): A NIOSH-approved organic vapor canister may be used to maintain vapor concentration below TLV.

Ventilation: Local Exhaust: To maintain vapor concentration below TLV.

Mechanical (General): Large amounts used to 0.2ppm.

Protective Clothing or Equipment: Safety glasses with side shield, Vinyl (polyethylene) non-sticking gloves, rubber apron to protect clothing.

Work/Hygienic Practices: Soap and water helps remove adhesive from skin.

NE = Not established

The data contained herein is based upon information that Pacer Technology believes to be reliable.

Users of this product have the responsibility to determine the suitability of use and to adopt all necessary precautions to ensure the safety and protection of property and persons involved in said use. All statements or suggestions are made without warranty, express or implied, regarding accuracy of the information, the hazards connected with the use of the material or the results to be obtained from the use thereof.

MATERIAL SAFETY DATA SHEET

05/15/08

Revision #9

Section 1 HAZARD RATING For Chemical Emergency Only:

PACER TECHNOLOGY In the US & Canada (800) 424-9300

9420 Santa Anita Avenue 2 Int'l & Wash DC (COLLECT) (703) 527-3887

Rancho Cucamonga, CA 91730 1 x 1 Telephone for Information :(909) 987-0550

PRODUCT IDENTIFICATION: Super Glue

Section 2 - HAZARDOUS INGREDIENTS INFORMATION:

Hazardous Components OSHA ACGIH OTHER %

(Common Names, CAS Number) PEL TLV LIMITS OPTION

Ethyl-2-Cyanoacrylate (7085-85-0) NE NE 0.2ppm TWA 60-100

Poly (Methyl Methacrylate) (9011-14-7) NE NE 10-30

Hydroquinone* (123-31-9) 2mg/m3 2mg/m3 0-1

*This ingredient is subject to the reporting requirements of Section 313 of Title III of the Superfund

Amendments & Reauthorization Act of 1986 (SARA) and 40 CFR 372.

Section 3 - PHYSICAL/CHEMICAL CHARACTERISTICS:

Boiling Point: 365 F Specific Gravity (H2O=1): 1.05

Vapor Density (Air=1): nil-NE Melting Point: NE

Vapor Pressure (mm Hg): 1 @ 20 C Evaporation Rate (Butyl acetate=1): nil-NE

Solubility in Water: Insoluble, material reacts to hardened mass for non-hazardous waste.

VOC: This product is VOC compliant for sale in California.

Appearance & Odor: Transparent water-white to straw colored liquid with stimulative odor.

Section 4 - FIRE AND EXPLOSION HAZARD DATA:

Flash Point (Method Used): 185 F (TCC) Flammable Limits: LEL: NE UEL: NE

Extinguishing Media: Flush with large amounts of water or dry chemical extinguisher.

Special Fire Fighting Procedures: Fumes may be irritating if not burning and require air supply with goggles while applying large amounts of water or dry chemical extinguisher.

Unusual Fire and Explosion Hazards: None. Combustible requiring the above procedures.

Section 5 - REACTIVITY DATA:

Stability: Stable XX Conditions to Avoid: Excessive heat above 176 F, moisture and alkalines. Stable up to 122 F. Store in a cool dry place.

Incompatibility (Materials to Avoid): Polymerized by water, alcohol, amines, alkaline materials and direct UV.

Hazardous Decomposition Products: Combustible by-products of carbon monoxide/dioxide.

Hazardous Polymerization: May Not Occur XX

Section 6 - HEALTH HAZARD DATA:

Route(s) of Entry: Inhalation: Yes Oral LD50 = > 5000 mg/kg (estimated)

Dermal LD50 = > 2000 mg/kg (estimated)

Health Hazards (Acute and Chronic):

Acute - Irritates eyes, mucous membranes.

Chronic - No residual effects of acute properties.

MATERIAL SAFETY DATA SHEET Super Glue Revision #9 Page 2 of 2

Carcinogenicity: NTP: No IARC Monographs: No OSHA Regulated: No

First Aid Procedures:

Eye contact - Tearing from eye irritation. Remove to fresh air. Flush areas of contact with water.

Adhesive will disassociate from eye/eyelids over time, usually within several hours. Temporary weeping of eyes/double vision may be experienced until clearance is achieved.

Skin contact - Immerse bonded areas in warm, soapy water. Peel or roll skin apart. Remove cured adhesive with several applications of warm, soapy water. Prolonged or repeated contact at elevated levels may cause dermatitis in sensitive individuals.

Inhalation - Irritation of mucous membranes/coughing. Remove to fresh air. Prolonged or repeated exposure at elevated levels may produce allergic reactions with asthma-like symptoms in sensitive individuals.

Ingestion - Lips may become stuck together: apply copious amounts of warm water & encourage wetting/pressure from saliva inside mouth. Peel or roll (do not pull) lips apart. It is almost impossible to swallow cyanoacrylate as adhesive solidifies upon contact with saliva & may adhere to inside of mouth. Saliva will lift adhesive in 1-2 days, avoid swallowing adhesive after detachment.

Medical Conditions Generally Aggravated by Exposure: Pre-existing skin, eye and respiratory

disorders may be aggravated by exposure.

Section 7 - PRECAUTIONS FOR SAFE HANDLING AND USE:

Steps to Be taken in Case Material is Released or Spilled: Polymerize with water. Solid material may be scraped from surface.

Waste Disposal Method: Incinerate solid combustible waste or dump as chemical waste according to local, state and federal regulations.

Precautions to Be Taken in Handling and Storing: Avoid contact with clothing as contact can cause burn. Avoid moisture, direct UV-sunlight and do not store above 25 C. Keep containers closed tightly when not in use. Ideal storage: 5-10 C.

Other Precautions: Avoid breathing vapor, contact with eyes/skin. Allow product to reach room temperature before use.

Section 8 - CONTROL MEASURES:

Respiratory Protection (Specify Type): A NIOSH-approved organic vapor canister may be used to maintain vapor concentration below TLV.

Ventilation: Local Exhaust: To maintain vapor concentration below TLV.

Mechanical (General): Large amounts used to 0.2ppm.

Protective Clothing or Equipment: Safety glasses with side shield, Vinyl (polyethylene) non-sticking gloves, rubber apron to protect clothing.

Work/Hygienic Practices: Soap and water helps remove adhesive from skin.

Section 9 - OTHER: Super Glue - Not regulated for transportation.

NE = Not established

The data contained herein is based upon information that Pacer Technology believes to be reliable.

Users of this product have the responsibility to determine the suitability of use and to adopt all necessary precautions to ensure the safety and protection of property and persons involved in said use. All statements or suggestions are made without warranty, express or implied, regarding accuracy of the information, the hazards connected with the use of the material or the results to be obtained from the use thereof.

MATERIAL SAFETY DATA SHEET

03/03/08

Rev 1

Section 1: For Chemical Emergency Only:

PACER TECHNOLOGY In the US & Canada (800) 424-9300

9420 Santa Anita Avenue Int'l & Wash DC (COLLECT) (703) 527-3887

Rancho Cucamonga, CA 91730 Telephone for Information: (909) 987-0550

PRODUCT IDENTIFICATION: HAZARD RATING 1

Z-Poxy 5 Minute Quick Shot Epoxy - Resin - Part A (PT36) 2 x 0

Section 2 - HAZARDOUS INGREDIENTS INFORMATION:

Hazardous Components OSHA ACGIH OTHER %

(Common Names, CAS Number) PEL TLV LIMITS OPTION

Bisphenol A/Epichlorohydrin: based epoxy resin* (25068-38-6) NE NE NE 60-100%

* This product is an epoxy resin produced by the condensation reaction of Epichlorohydrin and Bisphenol-A. These raw materials are consumed in the process. Residual levels of Epichlorohydrin are controlled to 1ppm, max., in the product.

Section 3 - PHYSICAL/CHEMICAL CHARACTERISTICS:

Boiling Point: >500F Specific Gravity (H2O=1): 1.17

Vapor Density (Air=1): NA Melting Point: NE

Vapor Pressure (mm Hg): 0.03 @ 77F Evaporation Rate (Butyl Acetate = 1): NA

Solubility in Water: Negligible.

Appearance & Odor: Light yellow colored viscous liquid.

Section 4 - FIRE AND EXPLOSION HAZARD DATA:

Flash Point (Method Used): 480F (PMCC) Flammable Limits: LEL: NE UEL: NE

Extinguishing Media: Water fog, foam, dry chemical or carbon dioxide.

Special Fire Fighting Procedures: Material will not burn unless preheated. Do not enter confined fire space without full bunker gear (helmet/face shield, bunker coat, gloves & rubber boats). Use positive pressure NIOSH-approved self-contained breathing apparatus. Cool fire exposed containers with water.

Unusual Fire and Explosion Hazards: Heating of resin above 300F in presence of air may cause slow oxidative decomposition. Above 500F polymerization may occur. Some curing agents, e.g. aliphatic amines can produce exothermic reactions which in large masses can cause runaway polymerization & charring of reactants. Fumes & vapors from these thermal & chemical decompositions vary widely in composition/toxicity. DO NOT BREATHE FUMES. Unidentified fumes & vapors may be toxic.

Section 5 - REACTIVITY DATA:

Stability: Stable XX Conditions to Avoid: Keep away from open flames & high temperatures.

Incompatibility (Materials to Avoid): Strong oxidizing agents, strong Lewis or mineral acids, strong mineral & organic bases, esp. primary & secondary aliphatic amines.

Hazardous Decomposition Products: Carbon monoxide, aldehydes, acids & other organic substances may be formed during combustion (>500F) temperature degradation.

Hazardous Polymerization: May Occur __ May Not Occur XX (Avoid heating >300F).

Section 6 - HEALTH HAZARD DATA:

Route(s) of Entry: Inhalation: YES Skin: YES Ingestion: YES

Health Hazards (Acute and Chronic):

Product moderately irritating to eyes, skin; contact with product at elevated temperatures can result in thermal burns; may cause skin sensitization; low order of acute oral toxicity noted; unlikely to be inhalation hazard due to low volatility.

Carcinogenicity: NTP: No IARC Monographs: No OSHA Regulated: No

Signs and Symptoms of Exposure & First Aid Procedures:

Eye contact - irritation: flush eyes with copious amounts of water for 15 min. while holding eyes open. Get medical attention immediately.

Skin contact - irritation/rash: remove contaminated clothing and wash with soap/water. Get medical attention if symptoms persist (contaminated leather articles i.e. shoes should be disposed of as contaminated waste). NOTE: hot product burns require immediate medical attention.

Inhalation - Remove to fresh air and provide oxygen if breathing is difficult. Get medical attention.

Ingestion - Do not induce vomiting. In general, no treatment, unless large amount is ingested, however, get medical advice.

NOTE TO PHYSICIAN: Emesis induction is normally not necessary in high viscosity, low volatility products, e.g. neat epoxy resins.

Medical Conditions Generally Aggravated by Exposure: Pre-existing eye/skin disorders or lung allergies.

Section 7 - PRECAUTIONS FOR SAFE HANDLING AND USE:

Steps to Be taken in Case Material is Released or Spilled: Product may burn although not readily ignitable. Use cautious judgment when cleaning up large spills, respirator and protective equipment as appropriate. Dike and contain material. Soak up residue with absorbent (clay, sand) materials and dispose of properly.

Waste Disposal Method: If product becomes waste, not considered hazardous waste by RCRA criteria (40 CFR 261). Dispose of according to federal, state and local regulations.

Precautions to Be Taken in Handling and Storing: Store in cool, dry place away from open flames and high temperatures.

Other Precautions: Empty containers may contain product residues & should be disposed of properly.

Section 8 - CONTROL MEASURES:

Respiratory Protection (Specify Type): Organic vapor respirator in areas with poor ventilation.

Ventilation: Local Exhaust: Good Mechanical (General): As needed.

Protective Clothing or Equipment: Safety glasses/goggles with side shields, chemically resistant gloves and other protective equipment to avoid direct contact.

Work/Hygienic Practices: Avoid contact with eyes or skin. Use in well ventilated area. Wash hands with soap and water after product use. Launder contaminated clothing before reuse and disposed of leather articles as contaminated waste.

NA = Not applicable

NE = Not established

The data contained herein is based upon information that Pacer Technology believes to be reliable.

Users of this product have the responsibility to determine the suitability of use and to adopt all necessary precautions to ensure the safety and protection of property and persons involved in said use. All statements or suggestions are made without warranty, express or implied, regarding accuracy of the information, the hazards connected with the use of the material or the results to be obtained from the use thereof.

MATERIAL SAFETY DATA SHEET

03/03/08

Rev. 1

Section 1: HAZARD RATING For Chemical Emergency Only:

PACER TECHNOLOGY 1 In the US & Canada (800) 424-9300

9420 Santa Anita Avenue 2 X 1 Int'l & Wash DC (COLLECT) (703) 527-3887

Rancho Cucamonga, CA 91730 Telephone for Information: (909) 987-0550

PRODUCT IDENTIFICATION: Z-Poxy 5 Min. Quick Shot Epoxy - Hardener - Part B

(PT36)

Section 2:  HAZARDOUS INGREDIENTS INFORMATION:

Hazardous Components OSHA ACGIH OTHER %

(Common Names, CAS Number) PEL TLV LIMITS OPTION

Proprietary Mercaptan Polymer NE NE 60-100

Tertiary Amine (90-72-2) NE NE 1-5

Note: Proprietary Mercaptan Polymer does not contain any ingredients subject to the reporting requirements of Section 313, Title III, part 372.

Section 3 - PHYSICAL/CHEMICAL CHARACTERISTICS:

Boiling Point: NE Specific Gravity (H2O=1): 1.13

Vapor Density (Air=1): NE Melting Point: NE

Vapor Pressure (mm Hg): NE Evaporation Rate (Butyl acetate = 1): NE

Solubility in Water: Slightly soluble.

Appearance & Odor: Light colored transparent syrup with mild sulfur odor.

Section 4 - FIRE AND EXPLOSION HAZARD DATA:

Flash Point (Method): 300 F (TCC) Flammable Limits: LEL: NE UEL: NE

Extinguishing Media: Water spray, carbon dioxide, foam or dry chemical.

Special Fire Fighting Procedures: Cool exposed containers with water spray. Wear self-contained breathing apparatus in confined areas.

Unusual Fire and Explosion Hazards: None known.

Section 5 - REACTIVITY DATA:

Stability: Stable XX Conditions to Avoid: Storage near large masses of epoxy resins.

Incompatibility (Materials to Avoid): Strong oxidants, amines especially when hot.

Hazardous Decomposition Products: Carbon monoxide/dioxide, hydrogen sulfide and oxides of sulfur.

Hazardous Polymerization: May Occur __ May Not Occur XX

Section 6 - HEALTH HAZARD DATA:

Route(s) of Entry: Inhalation: Yes Skin: Yes Ingestion: Yes

Health Hazards (Acute and Chronic):

Acute - irritates skin, eye & respiratory tract.

Chronic - May aggravate pre-existing skin/eye/lung conditions.

Carcinogenicity: NTP: No IARC Monographs: No OSHA Regulated: No

Signs and Symptoms of Exposure & First Aid Procedures:

Eye contact - Irritation: immediately flush eye with copious amounts of water for 15 minutes. Get medical attention.

Skin contact - Irritation upon direct contact. Remove contaminated clothing and wash affected areas with soap and water.

Inhalation - Remove to fresh air. Administer oxygen if available.

Ingestion - Do not induce vomiting. Keep airway clear if vomiting occurs.

Medical Conditions Generally Aggravated by Exposure: Pre-existing skin/eye/lung conditions.

Section 7 - PRECAUTIONS FOR SAFE HANDLING AND USE:

Steps to Be taken in Case Material is Released or Spilled: Stop leaks & contain spill. Soak up with absorbent material for disposal in proper container, wearing adequate protective clothing/respiratory protection.

Waste Disposal Method: In chemical landfill or incinerate in accordance with federal, state or local regulations.

Precautions to Be Taken in Handling and Storing: Do not store near epoxy resin, protect containers to avoid leaks and spills.

Other Precautions: CAUTION - May cause irritation. Avoid direct contact or breathing of mist or vapor. Use with adequate ventilation and use respiratory protection where mist or vapor may be generated. For industrial use only, keep containers closed when not in use.

Section 8 - CONTROL MEASURES:

Respiratory Protection (Specify Type): Organic vapor respirator to avoid inhalation of mist or vapor.

Ventilation: Local Exhaust: Good Mechanical (General): As needed.

Protective Clothing or Equipment: Safety glasses/goggles with side shields, rubber gloves, chemical resistant shoes and protective clothing to avoid direct contact.

Work/Hygienic Practices: Avoid direct contact or breathing of mist or vapor. Use with adequate ventilation. Wash hands with soap and water after use. Launder contaminated clothing before reuse. Do not take internally.

NE = Not established

The data contained herein is based upon information that Pacer Technology believes to be reliable.

Users of this product have the responsibility to determine the suitability of use and to adopt all necessary precautions to ensure the safety and protection of property and persons involved in said use. All statements or suggestions are made without warranty, express or implied, regarding accuracy of the information, the hazards connected with the use of the material or the results to be obtained from the use thereof.

MATERIAL SAFETY DATA SHEET

03/03/08

Revision #3

Section 1 For Chemical Emergency Only:

PACER TECHNOLOGY HAZARD RATING In the US & Canada (800) 424-9300

9420 Santa Anita Avenue 1 Int'l & Wash DC (COLLECT) (703) 527-3887

Rancho Cucamonga, CA 91730 2 x 0 Telephone for Information: (909) 987-0550

PRODUCT IDENTIFICATION: Z-Poxy 30 Minute Formula - Resin - Part A

Section 2 - HAZARDOUS INGREDIENTS INFORMATION:

Hazardous Components OSHA ACGIH OTHER %

(Common Names, CAS Number) PEL TLV LIMITS OPTION

Bisphenol A/Epichlorohydrin: based epoxy resin* (25068-38-6) NE NE NE 60-100%

* This product is an epoxy resin produced by the condensation reaction of Epichlorohydrin and

Bisphenol-A. These raw materials are consumed in the process. Residual levels of Epichlorohydrin are controlled to 1ppm, max, in the product.

Section 3 - PHYSICAL/CHEMICAL CHARACTERISTICS:

Boiling Point: >500F Specific Gravity (H2O=1): 1.17

Vapor Density (Air=1): NA Melting Point: NE

Vapor Pressure (mm Hg): 0.03 @ 77F Evaporation Rate (Butyl Acetate = 1): NA

Solubility in Water: Negligible.

Appearance & Odor: Light yellow colored viscous liquid.

Section 4 - FIRE AND EXPLOSION HAZARD DATA:

Flash Point (Method Used): 480F (PMCC) Flammable Limits: LEL: NE UEL: NE

Extinguishing Media: Water fog, foam, dry chemical or carbon dioxide.

Special Fire Fighting Procedures: Material will not burn unless preheated. Do not enter confined fire space without full bunker gear (helmet/face shield, bunker coat, gloves & rubber boats). Use positive pressure NIOSH-approved self-contained breathing apparatus. Cool fire exposed containers with water.

Unusual Fire and Explosion Hazards: Heating of resin above 300F in presence of air may cause slow oxidative decomposition. Above 500F polymerization may occur. Some curing agents, e.g. aliphatic amines can produce exothermic reactions which in large masses can cause runaway polymerization & charring of reactants. Fumes & vapors from these thermal & chemical decompositions vary widely in composition/toxicity. DO NOT BREATHE FUMES. Unidentified fumes & vapors may be toxic.

Section 5 - REACTIVITY DATA:

Stability: Stable XX Conditions to Avoid: Keep away from open flames & high temperatures.

Incompatibility (Materials to Avoid): Strong oxidizing agents, strong Lewis or mineral acids, strong mineral & organic bases, esp. primary & secondary aliphatic amines.

Hazardous Decomposition Products: Carbon monoxide, aldehydes, acids & other organic substances may be formed during combustion (>500F) temperature degradation.

Hazardous Polymerization: May Occur __ May Not Occur XX (Avoid heating >300F).

Section 6 - HEALTH HAZARD DATA:

Route(s) of Entry: Inhalation: YES Skin: YES Ingestion: YES

Health Hazards (Acute and Chronic):

Product moderately irritating to eyes, skin; contact with product at elevated temperatures can result in thermal burns; may cause skin sensitization; low order of acute oral toxicity noted; unlikely to be inhalation hazard due to low volatility.

Carcinogenicity: NTP: No IARC Monographs: No OSHA Regulated: No

First Aid Procedures:

Eye contact - irritation: flush eyes with copious amounts of water for 15 min. while holding eyes open. Get medical attention immediately.

Skin contact - irritation/rash: remove contaminated clothing and wash with soap/water. Get medical attention if symptoms persist (contaminated leather articles i.e. shoes should be disposed of as contaminated waste). NOTE: hot product burns require immediate medical attention.

Inhalation - Remove to fresh air and provide oxygen if breathing is difficult. Get medical attention.

Ingestion - Do not induce vomiting. In general, no treatment unless large amount is ingested, however, get medical advice.

NOTE TO PHYSICIAN: Emesis induction is normally not necessary in high viscosity, low volatility products, e.g. neat epoxy resins.

Medical Conditions Generally Aggravated by Exposure: Pre-existing eye/skin disorders or lung allergies.

Section 7 - PRECAUTIONS FOR SAFE HANDLING AND USE:

Steps to Be taken in Case Material is Released or Spilled: Product may burn although not readily ignitable. Use cautious judgment when cleaning up large spills. Respirator and protective equipment as appropriate. Dike and contain material. Soak up residue with absorbent (clay, sand) materials and dispose of properly.

Waste Disposal Method: If product becomes waste, not considered hazardous waste by RCRA criteria (40 CFR 261). Dispose of according to federal, state and local regulations.

Precautions to Be Taken in Handling and Storing: Store in cool, dry place away from open flames and high temperatures.

Other Precautions: Empty containers may contain product residues & should be disposed of properly.

Section 8 - CONTROL MEASURES:

Respiratory Protection (Specify Type): Organic vapor respirator in areas with poor ventilation.

Ventilation: Local Exhaust: Good Mechanical (General): As needed.

Protective Clothing or Equipment: Safety glasses/goggles with side shields, chemically resistant gloves and other protective equipment to avoid direct contact.

Work/Hygienic Practices: Avoid contact with eyes or skin. Use in well ventilated area. Wash hands with soap and water after product use. Launder contaminated clothing before reuse and disposed of leather articles as contaminated waste.

Section 9 - OTHER: Not restricted for transportation

NA = Not applicable

NE = Not established

The data contained herein is based upon information that Pacer Technology believes to be reliable. Users of this product have the responsibility to determine the suitability of use and to adopt all necessary precautions to ensure the safety and protection of property and persons involved in said use. All statements or suggestion are made without warranty, express or implied, regarding accuracy of the information, the hazards connected with the use of the material or the results to be obtained from the use thereof.

MATERIAL SAFETY DATA SHEET

03/03/08

Revision #5

Section 1.For Chemical Emergency Only:

PACER TECHNOLOGY HAZARD RATING In the US & Canada (800) 424-9300

9420 Santa Anita Avenue 1 Int'l & Wash DC (COLLECT) (703) 527-3887

Rancho Cucamonga, CA 91730 3 x 1 Telephone for Information: (909) 987-0550

PRODUCT IDENTIFICATION: Z-Poxy 30 Minute Formula - Hardener - Part B

Section 2 - HAZARDOUS INGREDIENTS INFORMATION:

Hazardous Components OSHA ACGIH OTHER %

(Common Names, CAS Number) PEL TLV LIMITS OPTION

Proprietary Mercaptan Polymer NE NE NE 60-100

Tertiary Amine (90-72-2) NE NE NE 5-10

Tris (Dimethyl Aminomethy) Phenol Trihexoate NE NE NE 1-5

+ This ingredient is subject to the reporting requirements of Section 313 of Title III of the Superfund

Amendments & Reauthorization Act of 1986 (SARA) and 40 CFR 372.

Section 3 - PHYSICAL/CHEMICAL CHARACTERISTICS:

Boiling Point: NE Specific Gravity (H2O=1): 1.13

Vapor Density (Air=1): NE Melting Point: NA

Vapor Pressure (mm Hg): NE Evaporation Rate (Butyl acetate = 1): NE

Solubility in Water: Slightly soluble.

Appearance & Odor: Viscous water white to light yellow liquid with mercaptan odor.

Section 4 - FIRE AND EXPLOSION HAZARD DATA:

Flash Point (Method): 300 F (TCC) Flammable Limits: LEL: NE UEL: NE

Extinguishing Media: Water spray, carbon dioxide, foam or dry chemical.

Special Fire Fighting Procedures: Cool exposed containers with water spray. Wear self-contained breathing apparatus in confined areas.

Unusual Fire and Explosion Hazards: None known.

Section 5 - REACTIVITY DATA:

Stability: Stable XX Conditions to Avoid: Storage near large masses of epoxy resins.

Incompatibility (Materials to Avoid): Strong oxidants, amines especially when hot.

Hazardous Decomposition Products: Carbon monoxide/dioxide, hydrogen sulfide and oxides of sulfur.

Hazardous Polymerization: May occur __ May Not Occur XX

Section 6 - HEALTH HAZARD DATA:

Route(s) of Entry: Inhalation: Yes Skin: Yes Ingestion: Yes

Health Hazards (Acute and Chronic):

Acute - irritates skin, eye & respiratory tract.

Chronic - May aggravate pre-existing skin/eye/lung conditions.

Carcinogenicity: NTP: No IARC Monographs: No OSHA Regulated: No

First Aid Procedures:

Eye contact - Irritation: immediately flush eye with copious amounts of water for 15 minutes. Get medical attention.

Skin contact - Irritation upon direct contact, remove contaminated clothing and wash affected areas with soap and water.

Inhalation - Remove to fresh air. Administer oxygen if available.

Ingestion - Do not induce vomiting. Keep airway clear if vomiting occurs.

Medical Conditions Generally Aggravated by Exposure: Pre-existing skin/eye/lung conditions.

Section 7 - PRECAUTIONS FOR SAFE HANDLING AND USE:

Steps to be taken in Case Material is Released or Spilled: Stop leaks & contain spill. Soak up with absorbent material for disposal in proper container, wearing adequate protective clothing/respiratory protection.

Waste Disposal Method: In chemical landfill or incinerate in accordance with federal, state or local regulations.

Precautions to Be Taken in Handling and Storing: Do not store near epoxy resin, protect containers to avoid leaks and spills.

Other Precautions: CAUTION - May cause irritation. Avoid direct contact or breathing of mist or vapor. Use with adequate ventilation and use respiratory protection where mist or vapor may be generated. For industrial use only. Keep containers closed when not in use.

Section 8 - CONTROL MEASURES:

Respiratory Protection (Specify Type): Organic vapor respirator to avoid inhalation of mist or vapor.

Ventilation: Local Exhaust: Good Mechanical (General): As needed.

Protective Clothing or Equipment: Safety glasses/goggles with side shields, rubber gloves, chemical resistant shoes and protective clothing to avoid direct contact.

Work/Hygienic Practices: Avoid direct contact or breathing of mist or vapor. Use with adequate ventilation. Wash hands with soap and water after use. Launder contaminated clothing before reuse.

Do not take internally.

Section 9 - OTHER: Not restricted for transportation

NE = Not established

The data contained herein is based upon information that Pacer Technology believes to be reliable.

Users of this product have the responsibility to determine the suitability of use and to adopt all necessary precautions to ensure the safety and protection of property and persons involved in said use. All statements or suggestions are made without warranty, express or implied, regarding accuracy of the information, the hazards connected with the use of the material or the results to be obtained from the use thereof.

MATERIAL SAFETY DATA SHEET

Kwik Epoxy Steel Resin VC-6

J-B Weld Company

P.O. Box 483

1130 Como Street

Sulphur Springs, TX 75482

Tel: (903) 885-7696

Fax: (903) 885-5911

SECTION I - IDENTIFICATION OF PRODUCT

PRODUCT NAME: J B WELD KWIK EPOXY STEEL RESIN - VC-6 PART A

PRODUCT CODE: (48009), 48149, 48151, 48177, 48190

REFERENCE: Resin Solution

SCHEDULE B NUMBER: 3506.91.0000

SECTION II - HAZARDOUS INGREDIENTS

INGREDIENTS WGT% CAS # TLV/PEL

Calcium Carbonate 40-50% 1317-65-3 ACGIH TLV: 10 mg/m3

OSHA: PEL 15 mppcf

Iron Powder 10-20% 65997-19-5 ACGIH TLV: 15 mg/m3

OSHA: PEL 15 mppcf

Epoxy Resin 30-40% 25068-38-6 N/E

Aromatic Hydrocarbons 1-5 % 64742-94-5 N/E

SECTION III - PHYSICAL DATA

APPEARANCE: Dark gray or black smooth paste

SPECIFIC GRAVITY: 1.80

VAPOR PRESSURE (mmHG): N/Av

BOILING POINT: N/E

VAPOR DENSITY (Air = 1): >1

EVAPORATION RATE (Ethyl Ether = 1): Slower than Ethyl Ether

VOLATILES BY WEIGHT: N/D

SOLUBILITY IN WATER: Not soluble

VOC: Grams/Liter = Nil

Lbs/Gallon = Nil

SECTION IV - FIRE AND EXPLOSION DATA

FLASH POINT: >200®F/93®C Seta Flash Closed cup

LOWER FLAMMABLE LIMIT %: N/E

UPPER FLAMMABLE LIMIT %: N/E

FIRE EXTINGUISHING MEDIA: Carbon Dioxide, Dry Chemical, Foam

SPECIAL FIRE FIGHTING PROCEDURES: Fight like a fuel oil fire. Cool fire exposed containers with water spray. Firefighter should wear OSHA/NIOSH approved self-contained breathing apparatus.

UNUSUAL FIRE AND EXPLOSION HAZARD: Closed containers exposed to high temperatures, such as fire conditions may rupture.

SECTION V - HEALTH HAZARD/TOXICOLOGICAL PROPERTIES

OVEREXPOSURE EFFECTS:

ACUTE EFFECTS:

EYES: Contact with eyes can cause severe irritation, possible irreparable eye damage.

SKIN: Contact with skin can cause irritation, (minor itching, burning and/or redness), Dermatitis,

defatting may be readily absorbed through the skin.

INHALATION: Inhalation of vapors can cause nasal and respiratory irritation, dizziness, weakness, fatigue, nausea, headache, possible unconsciousness and/or asphyxiation. Aspiration of material into lungs may result in chemical pneumonitis which can be fatal.

INGESTION: Ingestion can cause gastrointestinal irritation, nausea, vomiting, diarrhea.

CHRONIC EFFECTS:

Overexposure to this material has apparently been known to cause the following effects in lab animals: lung damage and/or allergic reaction

CARCINOGEN: YES _____ NO __X__

TERATOGEN: YES _____ NO __X__

MUTAGEN: YES _____ NO __X__

ROUTES OF EXPOSURE: skin, inhalation

FIRST AID:

INHALATION: If inhaled, remove victim from exposure to a well-ventilated area. Make them comfortably warm, but not hot. Use oxygen or artificial respiration as required. Consult a physician.

SKIN: For skin contact, wash promptly with soap and excess water.

EYES: For eye contact, flush promptly with excess water for at least fifteen minutes. Consult a physician.

INGESTION: If ingested, do not induce vomiting. Give victim a glass of water. Call a physician immediately.

SECTION V I - REACTIVITY DATA

STABILITY: Stable

CONDITIONS TO AVOID: Open flames, sparks, and heat.

INCOMPATIBILITY MATERIALS TO AVOID: Strong acids, alkalis, oxidizers.

HAZARDOUS DECOMPOSITION PRODUCTS: Carbon Dioxide, Carbon Monoxide and Carbon.

HAZARDOUS POLYMERIZATION: Will not occur.

SECTION VII - SPILL AND DISPOSAL PROCEDURE

SPILLS, LEAK OR RELEASE: Ventilate area. Remove all possible sources of ignition. Avoid prolonged breathing of vapor. Contain spill with inert absorbent.

WASTE DISPOSAL: Dispose of in accordance with local, state, and federal regulations.

SECTION VIII - PROTECTION INFORMATION

RESPIRATORY PROTECTION: If component TLV limits are exceeded, use NIOSH/MSHA approved respirator to remove vapors. Use an air-supplied respirator if necessary. With general ventilation, does not require a respirator.

VENTILATION: Use adequate ventilation in volume and pattern to keep TLV/PEL below recommended levels.

Explosion-proof ventilation may be necessary.

PROTECTIVE GLOVES: To prevent prolonged exposure use rubber gloves; solvents may be absorbed through the skin

EYE PROTECTION: Safety Glasses or goggles with splash guards or side shields.

OTHER PROTECTIVE EQUIPMENT: Wear protective clothing as required to prevent skin contact.

SECTION IX - HANDLING AND STORAGE PRECAUTIONS

STORAGE AND HANDLING: Use with adequate ventilation. Avoid contact with eyes and skin. Avoid breathing vapors. Do not store the product above 100®F/38®C. Do not flame, cut, braze weld or melt empty containers. Keep the product away from heat, open flame, and other sources of ignition. Avoid contact with strong acids, alkalis and oxidizers.

SECTION X - ADDITIONAL INFORMATION

SHIPPING INFORMATION: Please comply with DOT regulations in USA

HMIS RATING: Health 2 4 = Extreme

Fire 1 3 = High

Reactivity 1 2 = Moderate

1 = Slight

0 = Insignificant

Personal Protection - See Section VIII

CALIFORNIA PROPOSITION 65:

Trace amounts of epichlorohydrin, a chemical known to the State of California to cause cancer, is present in this product. However, given the low level and application of this product, typical uses do not constitute a significant risk under the standard.

SECTION 313 SUPPLIER NOTIFICATION:

This product contains the following toxic chemicals subject to the reporting requirements of the Emergency

Planning and Community Right-To-Know Act of 1986 and 40 CFR 372:

CHEMICAL NAME CAS % BY WGT

N/Ap

THIS INFORMATION MUST BE INCLUDED IN ALL MSDS THAT ARE COPIED AND DISTRIBUTED FOR THIS CHEMICAL

ABBREVIATIONS

IARC = International Agency for Research on Cancer

ACGIH = American Conference of Governmental Industrial Hygienists

NIOSH = National Institute of Occupational Safety and Health

TLV = Threshold Limit Value

PEL = Permissible Emission Level

DOT = Department of Transportation

NTP = National Toxicology Program

N/AV = Not Available

N/AP = Not Applicable

N/E = Not Established

N/D = Not Determined

PREPARED FOR: J-B Weld Company

P.O. Box 483

1130 Como Street

Sulphur Springs, TX 75482

Tel: (903) 885-7696

Fax: (903) 885-5911

REVIEWED ON May 17, 2004

SUPERSEDES March 1, 2003

REVISION Format

The information in the Material Safety Data Sheet has been compiled from our experience and from data presented in various technical publications. It is the user’s responsibility to determine the suitability of this information for the adoption of the safety precautions as may be necessary. We reserve the right to revise

Material Safety Data Sheets from time to time as new technical information becomes available. The user has the responsibility to contact the Company to make sure that the MSDS is the latest one issued.

MATERIAL SAFETY DATA SHEET

Kwik Epoxy Steel VC-6 Hardener – Part B

J-B Weld Company

P.O. Box 483

1130 Como Street

Sulphur Springs, TX 75482

Tel: (903) 885-7696

Fax: (903) 885-5911

SECTION I - IDENTIFICATION OF PRODUCT

PRODUCT NAME: J B WELD KWIK EPOXY STEEL HARDENER - PART B

PRODUCT CODE: (48094), 48148, 48150, 48178, 48191

REFERENCE: Epoxy Steel Hardener

SCHEDULE B NUMBER: 3214.10.0090

SECTION II - HAZARDOUS INGREDIENTS

INGREDIENTS WGT% CAS # TLV/PEL

Calcium Carbonate 5-10% 1317-65-3 ACGIH TWA 10 mg/m3

471-34-1 OSHA PEL 15 mppcf

Non-fibrous Talc 15-25% 14807-96-6 ACGIH TWA 2 mg/m3

OSHA PEL 20 mppcf

Barium Sulfate 35-45% 7727-43-7 ACGIH TWA 10 mg/m3

OSHA 15 mg/m3 Total dust

OSHA 15 mg/m3 Respirable dust

Alkyl Phenol 1-5 % 25154-52-3 N/E

Mercaptan terminated polymer 20-30% Trade Secret NE

2,4,6 [(Dimethylamino)methyl] phenol 1-5 % 90-72-2 N/E

Amorphous Silica 1-5 % 112945-52-5 ACGIH TWA 10 mg/m3

5 mg/m3 (respirable)

SECTION III - PHYSICAL DATA

APPEARANCE: White paste

SPECIFIC GRAVITY: 1.87

VAPOR PRESSURE (mmHG): N/Av

BOILING POINT: N/E

VAPOR DENSITY: Heavier than air

EVAPORATION RATE (Ethyl Ether = 1): Slower than Ethyl Ether

VOLATILES BY WEIGHT: Nil

SOLUBILITY IN WATER: Not soluble

VOC: Grams/Liter = 4

Lbs/Gallon = 0.03

SECTION IV - FIRE AND EXPLOSION DATA

FLASH POINT: >200°F/93°C Seta Flash Closed cup

LOWER FLAMMABLE LIMIT %: N/E

UPPER FLAMMABLE LIMIT %: N/E

FIRE EXTINGUISHING MEDIA: Carbon Dioxide, Dry Chemical, Foam

SPECIAL FIRE FIGHTING PROCEDURES: Fight like a fuel oil fire. Cool fire exposed containers with water

spray. Firefighter should wear OSHA/NIOSH approved self-contained breathing apparatus.

UNUSUAL FIRE AND EXPLOSION HAZARD: Closed containers exposed to high temperatures, such as fire conditions may rupture.

SECTION V - HEALTH HAZARD/TOXICOLOGICAL PROPERTIES

OVEREXPOSURE EFFECTS:

ACUTE EFFECTS:

EYES: Contact with eyes can cause severe irritation, possible irreparable eye damage.

SKIN: Contact with skin can cause irritation, (minor itching, burning and/or redness), Dermatitis,

defatting may be readily absorbed through the skin.

INHALATION: Inhalation of vapors can cause nasal and respiratory irritation, dizziness, weakness, fatigue, nausea, headache, possible unconsciousness and/or asphyxiation. Aspiration of material into lungs may result in chemical pneumonitis which can be fatal.

INGESTION: Ingestion can cause gastrointestinal irritation, nausea, vomiting, diarrhea.

CHRONIC EFFECTS:

Overexposure to this material has apparently been known to cause the following effects in lab animals: lung damage and/or allergic reaction

CARCINOGEN: YES _____ NO __X__

TERATOGEN: YES _____ NO __X__

MUTAGEN: YES _____ NO __X__

ROUTES OF EXPOSURE: skin, inhalation

FIRST AID:

INHALATION: If inhaled, remove victim from exposure to a well-ventilated area. Make them comfortably warm, but not hot. Use oxygen or artificial respiration as required. Consult a physician.

SKIN: For skin contact, wash promptly with soap and excess water.

EYES: For eye contact, flush promptly with excess water for at least fifteen minutes. Consult a physician.

INGESTION: If ingested, do not induce vomiting. Give victim a glass of water. Call a physician immediately.

SECTION V I - REACTIVITY DATA

STABILITY: Stable

CONDITIONS TO AVOID: Open flames, and heat.

INCOMPATIBILITY MATERIALS TO AVOID: Strong acids, alkalis, oxidizers.

HAZARDOUS DECOMPOSITION PRODUCTS: Carbon Dioxide, Carbon Monoxide and Carbon.

HAZARDOUS POLYMERIZATION: Will not occur.

SECTION VII - SPILL AND DISPOSAL PROCEDURE

SPILLS, LEAK OR RELEASE: Ventilate area. Remove all possible sources of ignition. Avoid prolonged breathing of vapor. Contain spill with inert absorbent.

WASTE DISPOSAL: Dispose of in accordance with local, state, and federal regulations.

SECTION VIII - PROTECTION INFORMATION

RESPIRATORY PROTECTION: If component TLV limits are exceeded, use NIOSH/MSHA approved respirator to remove vapors. Use an air-supplied respirator if necessary. With general ventilation, does not require a respirator.

VENTILATION: Use adequate ventilation in volume and pattern to keep TLV/PEL below recommended levels.

Explosion-proof ventilation may be necessary.

PROTECTIVE GLOVES: To prevent prolonged exposure use rubber gloves; solvents may be absorbed through the skin

EYE PROTECTION: Safety Glasses or goggles with splash guards or side shields.

OTHER PROTECTIVE EQUIPMENT: Wear protective clothing as required to prevent skin contact.

SECTION IX - HANDLING AND STORAGE PRECAUTIONS

STORAGE AND HANDLING: Use with adequate ventilation. Avoid contact with eyes and skin. Avoid breathing vapors. Do not store the product above 100°F/38°C. Do not flame, cut, braze weld or melt empty containers. Keep the product away from heat, open flame, and other sources of ignition. Avoid contact with strong acids, alkalis and oxidizers.

SECTION X - ADDITIONAL INFORMATION

SHIPPING INFORMATION: Please comply with DOT regulations in USA

HMIS RATING: Health 2 4 = Extreme

Fire 2 3 = High

Reactivity 2 2 = Moderate

1 = Slight

0 = Insignificant

Personal Protection - See Section VIII

CALIFORNIA PROPOSITION 65:

Trace amounts of some chemicals known to the State of California to cause cancer, birth defects or other reproductive harm may be present in this product.

SECTION 313 SUPPLIER NOTIFICATIONS:

This product contains the following toxic chemicals subject to the reporting requirements of the Emergency

Planning and Community Right-To-Know Act of 1986 and 40 CFR 372:

CHEMICAL NAME CAS % BY WGT

N/Ap

THIS INFORMATION MUST BE INCLUDED IN ALL MSDS THAT ARE COPIED AND DISTRIBUTED FOR THIS CHEMICAL

ABBREVIATIONS

IARC = International Agency for Research on Cancer

ACGIH = American Conference of Governmental Industrial Hygienists

NIOSH = National Institute of Occupational Safety and Health

TLV = Threshold Limit Value

PEL = Permissible Emission Level

DOT = Department of Transportation

NTP = National Toxicology Program

N/AV = Not Available

N/AP = Not Applicable

N/E = Not Established

N/D = Not Determined

PREPARED BY:

J-B Weld Company

P.O. Box 483

1130 Como Street

Sulphur Springs, TX 75482

Tel: (903) 885-7696

Fax: (903) 885-5911

REVIEWED ON May 17, 2004

SUPERSEDES March 1, 2003

REVISION Format

The information in the Material Safety Data Sheet has been compiled from our experience and from data presented in various technical publications. It is the user’s responsibility to determine the suitability of this information for the adoption of the safety precautions as may be necessary. We reserve the right to revise

Material Safety Data Sheets from time to time as new technical information becomes available. The user has the responsibility to contact the Company to make sure that the MSDS is the latest one issued.

MATERIAL SAFETY DATA SHEET

EPOXY STEEL HARDENER

J-B Weld Company

P.O. Box 483

1130 Como Street

Sulphur Springs, TX 75482

Tel: (903) 885-7696

Fax: (903) 885-5911

SECTION I - IDENTIFICATION OF PRODUCT

PRODUCT NAME: J B WELD EPOXY STEEL HARDENER

PRODUCT CODE: (48008), 48105, 48155, 48171

SYNONYM/CROSS REFERENCE: Epoxy Hardener

SCHEDULE B NUMBER: 3506.91.0000-3

SECTION II - HAZARDOUS INGREDIENTS

INGREDIENTS WGT% CAS # TLV/PEL

Calcium Carbonate 30-40% 1317-65-3 ACGIH TWA 10 mg/m3

OSHA PEL 15 mppcf

Barium Sulfate 20-30% 7727-43-7 ACGIH TWA 10 mg/m3

OSHA PEL 2 mppcf

Magnesium Silicate 5-10% 14807-96-6 ACGIH TWA 2 mg/m3

OSHA PEL 20 mppcf

Titanium Dioxide 1-5% 13463-67-7 ACGIH TWA 10 mg/m3

OSHA PEL 20 mg/m3

Zinc Sulfide 0-5% 1314-98-3 ACGIH TLV 10 mg/m3

Furfuryl Alcohol 1-5% 98-00-0 ACGIH TWA 10 ppm

Polyamide Resin 15-25% 68410-23-1 N/E

Aminophenols 1-5 % Mixture N/E

SECTION III - PHYSICAL DATA

APPEARANCE: White Paste

SPECIFIC GRAVITY: 1.78

VAPOR PRESSURE (mmHG): N/Av

BOILING POINT: N/Av

VAPOR DENSITY: Heavier than air

EVAPORATION RATE (Ethyl Ether = 1): Slower than Ethyl Ether

VOLATILES BY WEIGHT: Nil

SOLUBILITY IN WATER: Not Soluble

VOC: Grams/Liter = 72

Lbs/Gallon = 0.6

SECTION IV - FIRE AND EXPLOSION DATA

FLASH POINT: .>200°F/93°C Seta Flash Closed cup

LOWER FLAMMABLE LIMIT %: N/E

UPPER FLAMMABLE LIMIT %: N/E

FIRE EXTINGUISHING MEDIA: Carbon Dioxide, Dry Chemical, Foam

SPECIAL FIRE FIGHTING PROCEDURES: Fight like a fuel oil fire. Cool fire exposed containers with water spray. Firefighter should wear OSHA/NIOSH approved self-contained breathing apparatus.

UNUSUAL FIRE AND EXPLOSION HAZARD: Closed containers exposed to high temperatures, such as fire conditions may rupture.

SECTION V - HEALTH HAZARD/TOXICOLOGICAL PROPERTIES

OVEREXPOSURE EFFECTS:

ACUTE EFFECTS:

EYES: Contact with eyes can cause severe irritation, redness, tearing, blurred vision, and/or swelling. May cause eye damage.

SKIN: Contact with skin can cause irritation, (minor itching, burning and/or redness), Dermatitis, defatting may be readily absorbed through the skin.

INHALATION: Inhalation of vapors can cause nasal and respiratory irritation, dizziness, weakness, fatigue, nausea, headache, possible unconsciousness and/or asphyxiation. Aspiration of material into lungs may result in chemical pneumonitis which can be fatal.

INGESTION: Ingestion can cause gastrointestinal irritation, nausea, vomiting, diarrhea.

CHRONIC EFFECTS:

Overexposure to this material has apparently been known to cause the following effects in lab animals: Eye damage, skin damage.

CARCINOGEN: YES _____ NO __X__

TERATOGEN: YES _____ NO __X__

MUTAGEN: YES _____ NO __X__

PRIMARY ROUTES OF EXPOSURE: Skin, inhalation

FIRST AID:

INHALATION: If inhaled, remove victim from exposure to a well-ventilated area. Make them comfortably warm, but not hot. Use oxygen or artificial respiration as required. Consult a physician.

SKIN: For skin contact, wash promptly with soap and excess water.

EYES: For eye contact, flush promptly with excess water for at least fifteen minutes. Consult a physician.

INGESTION: If ingested, do not induce vomiting. Give victim a glass of water. Call a physician immediately.

SECTION V I - REACTIVITY DATA

STABILITY: Stable

CONDITIONS TO AVOID: Open flames, sparks, heat, electrical and static discharge.

INCOMPATIBILITY MATERIALS TO AVOID: Strong acids, alkalis, oxidizers.

HAZARDOUS DECOMPOSITION PRODUCTS: Carbon Dioxide, Carbon Monoxide and Carbon.

HAZARDOUS POLYMERIZATION: Will not occur.

SECTION VII - SPILL AND DISPOSAL PROCEDURE

SPILLS, LEAK OR RELEASE: Ventilate area. Remove all possible sources of ignition. Avoid prolonged breathing of vapor. Contain spill with inert absorbent.

WASTE DISPOSAL: Dispose of in accordance with local, state, and federal regulations.

SECTION VIII - PROTECTION INFORMATION

RESPIRATORY PROTECTION: If component TLV limits are exceeded, use NIOSH/MSHA approved respirator to remove vapors. Use an air-supplied respirator if necessary.

VENTILATION: Use adequate ventilation in volume and pattern to keep TLV/PEL below recommended levels.

Explosion-proof ventilation may be necessary.

PROTECTIVE GLOVES: To prevent prolonged exposure use rubber gloves; solvents may be absorbed through the skin

EYE PROTECTION: Safety Glasses or goggles with splash guards or side shields.

OTHER PROTECTIVE EQUIPMENT: Wear protective clothing as required to prevent skin contact.

SECTION IX - HANDLING AND STORAGE PRECAUTIONS

STORAGE AND HANDLING: Use with adequate ventilation. Avoid contact with eyes and skin. Avoid breathing vapors. Do not store the product above 100°F/38°C. Do not flame, cut, braze weld or melt empty containers. Keep the product away from heat, open flame, and other sources of ignition. Avoid contact with strong acids, alkalis and oxidizers.

SECTION X - ADDITIONAL INFORMATION

SHIPPING INFORMATION: Please comply with DOT regulations in USA

HMIS RATING: Health 2 4 = Extreme

Fire 1 3 = High

Reactivity 1 2 = Moderate

1 = Slight

0 = Insignificant

Personal Protection - See Section VIII

CALIFORNIA PROPOSITION 65:

Trace amounts of some chemicals known to the State of California to cause cancer, birth defects

or other reproductive harm may be present in this product.

SECTION 313 SUPPLIER NOTIFICATION:

This product contains the following toxic chemicals subject to the reporting requirements of the Emergency

Planning and Community Right-To-Know Act of 1986 and 40 CFR 372:

CHEMICAL NAME CAS % BY WGT

NOT APPLICABLE

THIS INFORMATION MUST BE INCLUDED IN ALL MSDS THAT ARE COPIED AND DISTRIBUTED FOR THIS CHEMICAL

ABBREVIATIONS

IARC = International Agency for Research on Cancer

ACGIH = American Conference of Governmental Industrial Hygienists

NIOSH = National Institute of Occupational Safety and Health

TLV = Threshold Limit Value

PEL = Permissible Emission Level

DOT = Department of Transportation

NTP = National Toxicology Program

N/AV = Not Available

N/AP = Not Applicable

N/E = Not Established

N/D = Not Determined

PREPARED FOR:

J-B Weld Company

P.O. Box 483

1130 Como Street

Sulphur Springs, TX 75482

Tel: (903) 885-7696

Fax: (903) 885-5911

REVIEWED ON May 17, 2004

SUPERSEDES June 23, 2003

REVISION Format

The information in the Material Safety Data Sheet has been compiled from our experience and from data presented in various technical publications. It is the user’s responsibility to determine the suitability of this information for the adoption of the safety precautions as may be necessary. We reserve the right to revise

Material Safety Data Sheets from time to time as new technical information becomes available. The user has the responsibility to contact the Company to make sure that the MSDS is the latest one issued.

MATERIAL SAFETY DATA SHEET

Page 1 Epoxy Steel Resin

J-B Weld Company

P.O. Box 483

1130 Como Street

Sulphur Springs, TX 75482

Tel: (903) 885-7696

Fax: (903) 885-5911

SECTION I - IDENTIFICATION OF PRODUCT

PRODUCT NAME: JB WELD - EPOXY STEEL RESIN

PRODUCT CODE: (48009), 48102, 48153, 48170

SYNONYM/CROSS REFERENCE: Resin Solution

SCHEDULE B NUMBER: 3506.91.0000

SECTION II - HAZARDOUS INGREDIENTS

INGREDIENTS WGT% CAS # TLV/PEL

Calcium Carbonate 40-50% 1317-65-3 ACGIH: TWA 10 mg/m3

OSHA: PEL 15 mppcf

Iron Powder 10-20% 65997-19-5 ACGIH TLV 15 mg/m3

OSHA: PEL 15 mppcf

Epoxy Resin 30-40% 25068-38-6 N/E

Aromatic Hydrocarbons 1-5 % 64742-94-5 N/E

SECTION III - PHYSICAL DATA

APPEARANCE: Dark gray or black smooth paste

SPECIFIC GRAVITY: 1.80

VAPOR PRESSURE (mmHG): N/Av

BOILING POINT: N/E

VAPOR DENSITY: Heavier than air

EVAPORATION RATE (Ethyl Ether = 1): Slower than Ethyl Ether

VOLATILES BY WEIGHT: N/D

SOLUBILITY IN WATER: Not Soluble

VOC: Grams/Liter = Nil

Lbs/Gallon = Nil

SECTION IV - FIRE AND EXPLOSION DATA

FLASH POINT: >200°F/ 93°C Seta Flash Closed cup

LOWER FLAMMABLE LIMIT %: N/E

UPPER FLAMMABLE LIMIT %: N/E

FIRE EXTINGUISHING MEDIA: Carbon Dioxide, Dry Chemical, Foam

SPECIAL FIRE FIGHTING PROCEDURES: Fight like a fuel oil fire. Cool fire exposed containers with water spray. Firefighter should wear OSHA/NIOSH approved self-contained breathing apparatus.

UNUSUAL FIRE AND EXPLOSION HAZARD: Closed containers exposed to high temperatures, such as fire conditions may rupture.

SECTION V - HEALTH HAZARD/TOXICOLOGICAL PROPERTIES

OVEREXPOSURE EFFECTS:

ACUTE EFFECTS:

EYES: Contact with eyes can cause irritation, redness, tearing, blurred vision, and/or swelling.

SKIN: Contact with skin can cause irritation, (minor itching, burning and/or redness), Dermatitis,

defatting may be readily absorbed through the skin.

INHALATION: Inhalation of vapors can cause nasal and respiratory irritation, dizziness, weakness, fatigue, nausea, headache, possible unconsciousness and/or asphyxiation. Aspiration of material into lungs may result in chemical pneumonitis which can be fatal.

INGESTION: Ingestion can cause gastrointestinal irritation, nausea, vomiting, diarrhea.

CHRONIC EFFECTS:

Overexposure to this material has apparently been known to cause the following effects in lab animals: skin sensitization, respiratory system irritation.

CARCINOGEN: YES _____ NO __X__

TERATOGEN: YES _____ NO __X__

MUTAGEN: YES _____ NO __X__

PRIMARY ROUTES OF EXPOSURE: skin, inhalation, eyes

FIRST AID:

INHALATION: If inhaled, remove victim from exposure to a well-ventilated area. Make them comfortably warm, but not hot. Use oxygen or artificial respiration as required. Consult a physician.

SKIN: For skin contact, wash promptly with soap and excess water.

EYES: For eye contact, flush promptly with excess water for at least fifteen minutes. Consult a physician.

INGESTION: If ingested, do not induce vomiting. Give victim a glass of water. Call a physician immediately.

SECTION V I - REACTIVITY DATA

STABILITY: Stable

CONDITIONS TO AVOID: Open flames & heat. .

INCOMPATIBILITY MATERIALS TO AVOID: Strong acids, alkalis, oxidizers.

HAZARDOUS DECOMPOSITION PRODUCTS: Carbon Dioxide, Carbon Monoxide and Carbon.

HAZARDOUS POLYMERIZATION: Will not occur.

SECTION VII - SPILL AND DISPOSAL PROCEDURE

SPILLS, LEAK OR RELEASE: Ventilate area. Remove all possible sources of ignition. Avoid prolonged breathing of vapor. Contain spill with inert absorbent.

WASTE DISPOSAL: Dispose of in accordance with local, state, and federal regulations.

SECTION VIII - PROTECTION INFORMATION

RESPIRATORY PROTECTION: If component TLV limits are exceeded, use NIOSH/MSHA approved respirator to remove vapors. Use an air-supplied respirator if necessary. With general ventilation, does not require a respirator.

VENTILATION: Use adequate ventilation in volume and pattern to keep TLV/PEL below recommended levels.

PROTECTIVE GLOVES: To prevent prolonged exposure use rubber gloves; solvents may be absorbed through the skin

EYE PROTECTION: Safety Glasses or goggles with splash guards or side shields.

OTHER PROTECTIVE EQUIPMENT: Wear protective clothing as required to prevent skin contact.

SECTION IX - HANDLING AND STORAGE PRECAUTIONS

STORAGE AND HANDLING: Use with adequate ventilation. Avoid contact with eyes and skin. Avoid breathing vapors. Do not store the product above 100®F/38®C. Do not flame, cut, braze weld or melt empty containers. Keep the product away from heat, open flame, and other sources of ignition. Avoid contact with strong acids, alkalis and oxidizers.

SECTION X - ADDITIONAL INFORMATION

SHIPPING INFORMATION: Please comply with DOT regulations in USA

HMIS RATING: Health 2 4 = Extreme

Fire 1 3 = High

Reactivity 1 2 = Moderate

1 = Slight

0 = Insignificant

Personal Protection - See Section VIII

CALIFORNIA PROPOSITION 65:

Trace amounts of epichlorohydrin, a chemical known to the State of California to cause cancer, are present in this product. However, given the low level and application of this product, typical uses do not constitute a significant risk under the standard.

SECTION 313 SUPPLIER NOTIFICATION:

This product contains the following toxic chemicals subject to the reporting requirements of the Emergency

Planning and Community Right-To-Know Act of 1986 and 40 CFR 372:

CHEMICAL NAME CAS % BY WGT

Not Applicable

THIS INFORMATION MUST BE INCLUDED IN ALL MSDS THAT ARE COPIED AND DISTRIBUTED FOR THIS CHEMICAL

ABBREVIATIONS

IARC = International Agency for Research on Cancer

ACGIH = American Conference of Governmental Industrial Hygienists

NIOSH = National Institute of Occupational Safety and Health

TLV = Threshold Limit Value

PEL = Permissible Emission Level

DOT = Department of Transportation

NTP = National Toxicology Program

N/AV = Not Available

N/AP = Not Applicable

N/E = Not Established

N/D = Not Determined

PREPARED FOR: J-B Weld Company

P.O. Box 483

1130 Como Street

Sulphur Springs, TX 75482

Tel: (903) 885-7696

Fax: (903) 885-5911

REVIEWED ON May 17, 2004

SUPERSEDES March 1, 2003

REVISION Format

The information in the Material Safety Data Sheet has been compiled from our experience and from data presented in various technical publications. It is the user’s responsibility to determine the suitability of this information for the adoption of the safety precautions as may be necessary. We reserve the right to revise

Material Safety Data Sheets from time to time as new technical information becomes available. The user has the responsibility to contact the Company to make sure that the MSDS is the latest one issued.

M A T E R I A L S A F E T Y D A T A S H E E T

2.1 VOC HI SOLIDS ACRYLIC LACQUER - GRAY Page: 1

2/26/2008

PRODUCT NAME: 2.1 VOC HI SOLIDS ACRYLIC LACQUER - GRAY HMIS CODES: H F R P

5 STAR Part Number: FS-5400C-G 2*3 0 G

SECTION I - MANUFACTURER IDENTIFICATION\

MANUFACTURED FOR : ABI/Autobody Brands International

A division of IAMG/International Autobody Marketing Group

ADDRESS : 9419 E. SAN SALVADOR DR. SUITE 104

SCOTTSDALE, AZ 85258

EMERGENCY PHONE : (800)424-9300 (24 hrs.) DATE PRINTED : 2/26/2008

INFORMATION PHONE : 1-87-REFINISH PREPARER NAME: MSDS Coordinator

SECTION II - HAZARDOUS INGREDIENTS/SARA III INFORMATION

VAPOR PRESSURE WEIGHT

REPORTABLE COMPONENTS CAS NUMBER mm Hg @ TEMP PERCENT

------------------------------------------------------------------------------------------------------------------------

ACETONE 67-64-1 185 68 F 48.34

ACGIH TLV STEL: 750 ppm

ACGIH TLV TWA: 500 ppm

OSHA VPEL TWA: 750 ppm

OSHA VPEL STEL: 1000 ppm

p-chloro-a,a,a-trifluorotoluene 98-56-6 N/A N/A 5%-15%

ACGIH TLV: 2.5 mg/m3 TWA AS FLUORIDES

OSHA PEL: 2.5 mg/m3 TWA AS FLUORIDES

NIOSH: 2.5 mg/m3 TWA AS FLUORIDES

talc 14807-96-6 N/A 0%-10%

ACGIH TLV: 2 mg/m3 TWA RESPIRABLE DUST

OSHA PEL: 20 mppcf

NITROCELLULOSE 9004-70-0 N/D N/D 5.08

magnesite dust 546-93-0 N/A N/A 0%-10%

OSHA PEL: 15 mg/m3 (TOTAL DUST)

OSHA PEL: 5 mg/m3 (RESPIRABLE DUST)

ACGIH TLV: 10 mg/m3 (TOTAL DUST)

NIOSH: 10 mg/m3 TWA (TOTAL DUST)

NIOSH: 5 mg/m3 TWA (RESPIRABLE DUST)

titanium dioxide 13463-67-7 N/A 0%-10%

OSHA PEL: 10 mg/m3 TWA (TOTAL DUST)

ISOPROPYL ALCOHOL 67-63-0 32 68 F 2.18

OSHA PEL: 400 ppm TWA

ACGIH TLV: 400 ppm TWA

ACGIH TLV: 500 ppm STEL

OSHA PEL: 500 ppm

OSHA STEL: 500 ppm

* di-n-butylphthalate 84-74-2 0.8 302 F 1.94

* XYLENES 1330-20-7 5.10 68 F 1.26

ACGIH TWA 100 ppm

ACGIH STEL 150 ppm

OSHA TWA 100 ppm

OSHA STEL 150 ppm

ETHYL BENZENE 100-41-4 5.1 68 F .26

OSHA PEL: 100 ppm TWA

ACGIH TVL: 100 ppm TWA

PHOSPHORIC ACID 7664-38-2 0.03 68 F .21

OSHA PEL: 1.000 mg/m3 TWA

ACGIH TLV: 1.000 mg/m3 TWA

ACGIH TLV: 3.000 mg/m3 STEL

TOLUENE 108-88-3 22 68 F .16

ACGIH TLV: 150 ppm STEL (SKIN)

ACGIH TLV: 50 ppm TWA (SKIN)

OSHA VPEL: 150 ppm STEL

OSHA VPEL: 100 ppm TWA

SILICA, QUARTZ 14808-60-7 N/A N/A .1493

OSHA PEL: 30 mg/m3 TOTAL DUST

OSHA PEL: 10 mg/m3 RESPIRABLE DUST

ACGIH TLV: 0.1 mg/m3 TWA RESPIRABLE DUST

pseudocumene 95-63-6 1.58 68 F .02

ACGIH TLV: 25 ppm TWA

OSHA PEL: 25 ppm TWA

NIOSH: 25 ppm TWA

NIOSH: 125 mg/m3 TWA

SILICA, CRISTOBALITE 14464-46-1 N/A N/A .001

OSHA PEL: 0.05 mg/m3 RESPIRABLE DUST

ACGIH TLV: 0.05 mg/m3 TWA RESPIRABLE DUST

* Indicates toxic chemical(s) subject to the reporting requirements of section 313 of Title III and of 40 CFR 372.

N/A

SECTION III - PHYSICAL/CHEMICAL CHARACTERISTICS

BOILING RANGE: 133 F - 377.6 F SPECIFIC GRAVITY (H2O=1): 1.06

VAPOR DENSITY: Heavier than air EVAPORATION RATE: Slower than ether

V.O.C. grams/liter: 195.29 V.O.C. lbs./gal.: 1.63

SOLUBILITY IN WATER: Insoluble SOLIDS BY VOLUME: 19.217

APPEARANCE AND ODOR: Opaque liquid with an organic solvent odor.

SECTION IV - FIRE AND EXPLOSION HAZARD DATA

FLASH POINT: -4.0 F METHOD USED: TAGCC

FLAMMABLE LIMITS IN AIR BY VOLUME- LOWER: 0.90 UPPER: 12.8

EXTINGUISHING MEDIA: Foam, Carbon Dioxide, Dry Chemical, Water Fog

SPECIAL FIREFIGHTING PROCEDURES

Full protective equipment, including self contained breathing apparatus, is recommended. Water from fog nozzles may be used to cool closed containers to prevent pressure build up.

UNUSUAL FIRE AND EXPLOSION HAZARDS

When heated above flashpoint, emits flammable vapors which, when mixed with air, can burn or become explosive. Fine mists or sprays may be flammable below the flash point.

SECTION V - REACTIVITY DATA

STABILITY: Stable

CONDITIONS TO AVOID

Avoid all sources of ignition

INCOMPATIBILITY (MATERIALS TO AVOID)

Strong oxidizing materials

HAZARDOUS DECOMPOSITION OR BYPRODUCTS

May produce hazardous fumes when heated to decomposition. Fumes may contain Carbon Monoxide and Carbon Dioxide.

HAZARDOUS POLYMERIZATION: Will not occur

SECTION VI - HEALTH HAZARD DATA

INHALATION HEALTH RISKS AND SYMPTOMS OF EXPOSURE

May cause nose and throat irritation. Repeated and prolonged exposure to organic solvents may lead to permanent brain and nervous system damage. Eye watering, headaches, nausea, dizziness, and loss of coordination are signs that solvent levels are too high.

Individuals with breathing problems must not be exposed to this product. If affected by inhalation, remove to fresh air.

If breathing difficulty persists, consult a physician.

SKIN AND EYE CONTACT HEALTH RISKS AND SYMPTOMS OF EXPOSURE

May cause irritation or burning of the eyes. Repeated and prolonged skin contact may cause skin irritation or dermatitis. In case of eye contact, immediately flush eyes with plenty of water for at least 15 minutes; call a physician. In case of skin contact, wash with soap and water. If irritation occurs, contact a physician.

INGESTION HEALTH RISKS AND SYMPTOMS OF EXPOSURE

Gastrointestinal distress. In the unlikely event of ingestion, call a physician immediately and have the names of all ingredients available.

HEALTH HAZARDS (ACUTE AND CHRONIC)

ACUTE- Dizziness, irritation of the respiratory tract, weakness, nausea, or possible narcosis or even asphyxiation. May be accompanied by coughing or labored breathing.

CHRONIC- Reports have linked organic solvents with brain and nervous system damage. Misuse of this product by deliberately concentrating and inhaling the contents may be harmful or fatal.

CARCINOGENICITY: NTP CARCINOGEN: Yes IARC MONOGRAPHS: Yes

PROPOSITION 65 STATEMENT: WARNING! This product contains a chemical or chemicals known to the state of California to cause cancer and/or birth defects or other reproductive harm.

OSHA REGULATED: Yes

MEDICAL CONDITIONS GENERALLY AGGRAVATED BY EXPOSURE

Do not use this product if you have chronic lung or breathing problems.

EMERGENCY AND FIRST AID PROCEDURES

If ingestion, or any type of overexposure or symptoms of overexposure occur during the use of this product, contact a poison control center, emergency room or physician immediately; have material safety data sheet available.

SECTION VII - PRECAUTIONS FOR SAFE HANDLING AND USE

STEPS TO BE TAKEN IN CASE MATERIAL IS RELEASED OR SPILLED

Remove all sources of ignition (sparks, flames, and hot surfaces). Avoid breathing vapors. Ventilate area. Remove with inert absorbent and non-sparking tools.

WASTE DISPOSAL METHOD

Dispose in accordance with state , federal and local regulations. Do not incinerate closed containers.

PRECAUTIONS TO BE TAKEN IN HANDLING AND STORING

Keep containers tightly closed in a cool, dry, well ventilated area away from all possible ignition sources. Store large

quanaties of material in buildings designed for the storage of flammable liquids.

OTHER PRECAUTIONS

Employees should be trained in safety measures that should be taken when using this product.

SECTION VIII - CONTROL MEASURES

RESPIRATORY PROTECTION

Avoid breathing vapors or spray mist. Wear a properly fitted respirator approved by NIOSH/MSHA (TC-23c) for use with paints during application and until all vapors are exhausted. In confined areas, or where continuous spray operations are typical, or proper respirator fit is not possible, wear a positive-pressure supplied air respirator (TC-19c). In all cases follow respirator manufactures directions for respirator use. Do not allow anyone without protection into the painting area.

VENTILATION

Provide sufficient ventilation to keep contaminates below applicable OSHA requirements.

PROTECTIVE GLOVES

Neoprene gloves impervious to organic solvents are recommended.

EYE PROTECTION

Use safety eyewear designed to protect against liquid splash.

OTHER PROTECTIVE CLOTHING OR EQUIPMENT

Impervious coveralls are recommended.

WORK/HYGIENIC PRACTICES

Eye wash and safety showers in the work place are recommended. Wash hands before eating and smoking.

SECTION IX - DISCLAIMER

The information contained in this material safety data sheet is information from our suppliers and other sources. It is believed to be reliable. This data is not to be taken as a warranty or representation for which this company assumes legal responsibility.

DIMENSION® PRO NR Acrylic Enamel D6/W

Continued IV-93

Material Safety Data Sheet

2006

Section 1 -- Product and Company Identification

PRODUCT NUMBER HMIS CODES

Health 2*

D6/W Flammability 3

Reactivity 0

PRODUCT NAME

DIMENSION® PRO NR Acrylic Enamel, All Colors

MANUFACTURER'S NAME EMERGENCY TELEPHONE NO.

WESTERN AUTOMOTIVE FINISHES (216) 566-2917

101 Prospect Avenue N.W.

Cleveland, OH 44115

DATE OF PREPARATION INFORMATION TELEPHONE NO.

14-NOV-06 (216) 566-2902

Section 2 -- Composition/Information on Ingredients

% by WT CAS No. INGREDIENT UNITS VAPOR PRESSURE

1-5 64742-88-7 Mineral Spirits

ACGIH TLV 100 ppm 2 mm

OSHA PEL 100 ppm

0-2 108-88-3 Toluene

ACGIH TLV 50 ppm (Skin) 22 mm

OSHA PEL 100 ppm (Skin)

OSHA PEL 150 ppm (Skin) STEL

4-5 100-41-4 Ethylbenzene

ACGIH TLV 100 ppm 7.1 mm

ACGIH TLV 125 ppm STEL

OSHA PEL 100 ppm

OSHA PEL 125 ppm STEL

20-30 1330-20-7 Xylene

ACGIH TLV 100 ppm 5.9 mm

ACGIH TLV 150 ppm STEL

OSHA PEL 100 ppm

OSHA PEL 150 ppm STEL

1-2 111-76-2 2-Butoxyethanol

ACGIH TLV 20 ppm 0.88 mm

OSHA PEL 25 ppm

5-10 67-64-1 Acetone

ACGIH TLV 500 ppm 180 mm

ACGIH TLV 750 ppm STEL

OSHA PEL 1000 ppm

0.5-1 107-87-9 Methyl n-Propyl Ketone

ACGIH TLV 200 ppm 27.8 mm

ACGIH TLV 250 ppm STEL

OSHA PEL 200 ppm

OSHA PEL 250 ppm STEL

2-10 123-86-4 n-Butyl Acetate

ACGIH TLV 150 ppm 10 mm

ACGIH TLV 200 ppm STEL

OSHA PEL 150 ppm

OSHA PEL 200 ppm STEL

0.5-2 112-07-2 2-Butoxyethyl Acetate

ACGIH TLV Not Available 1 mm

OSHA PEL Not Available

0-5 Proprietary Coated Mica

ACGIH TLV 3 mg/m3 as Dust

OSHA PEL 3 mg/m3 as Dust

0-26 13463-67-7 Titanium Dioxide

ACGIH TLV 10 mg/m3 as Dust

OSHA PEL 10 mg/m3 Total Dust

OSHA PEL 5 mg/m3 Respirable Fraction

0-1 1333-86-4 Carbon Black

ACGIH TLV 3.5 mg/m3

OSHA PEL 3.5 mg/m3

0-10 8007-18-9 Nickel Antimony Titanate

ACGIH TLV 0.5 mg/m3

OSHA PEL 0.5 mg/m3

-------------------------------------

0.9 maximum Antimony (as Sb)

CERTAIN COLORS CONTAIN LEAD AND CHROMIUM (see PRODUCT LABEL)

<10 1344-37-2 Lead Chromate

ACGIH TLV 0.05 mg/m3

OSHA PEL 0.05 mg/m3

<17 12656-85-8 Molybdate Orange

ACGIH TLV 0.05 mg/m3

OSHA PEL 0.05 mg/m3

-------------------------------------

9.6 maximum Lead (as Pb)

2.0 maximum Chromium VI (as Cr)

Section 3 -- Hazards Identification

ROUTES OF EXPOSURE

INHALATION of vapor or spray mist.

EYE or SKIN contact with the product, vapor or spray mist.

EFFECTS OF OVEREXPOSURE

EYES: Irritation.

SKIN: Prolonged or repeated exposure may cause irritation.

INHALATION: Irritation of the upper respiratory system.

May cause nervous system depression. Extreme overexposure may result in unconsciousness and possibly death.

Certain colors contain Lead (see PRODUCT LABEL). Acute occupational exposure to Lead is uncommon, but results in effects and symptoms similar to chronic overexposure described below.

SIGNS AND SYMPTOMS OF OVEREXPOSURE

Headache, dizziness, nausea, and loss of coordination are indications of excessive exposure to vapors or spray mists.

Redness and itching or burning sensation may indicate eye or excessive skin exposure.

MEDICAL CONDITIONS AGGRAVATED BY EXPOSURE

May cause allergic respiratory and/or skin reaction in susceptible persons or sensitization. This effect may be delayed several hours after exposure.

CANCER INFORMATION

For complete discussion of toxicology data refer to Section 11.

Section 4 -- First Aid Measures

EYES: Flush eyes with large amounts of water for 15 minutes.

Get medical attention.

SKIN: Wash affected area thoroughly with soap and water.

Remove contaminated clothing and launder before re-use.

INHALATION: If any breathing problems occur during use, LEAVE THE

AREA and get fresh air. If problems remain or occur later, IMMEDIATELY get medical attention.

INGESTION: Do not induce vomiting.

Get medical attention immediately.

Section 5 -- Fire Fighting Measures

FLASH POINT LEL UEL

5-10 °F TCC 0.5 12.8

FLAMMABILITY CLASSIFICATION

RED LABEL -- Extremely Flammable, Flash below 21 °F (-6 °C)

EXTINGUISHING MEDIA

Carbon Dioxide, Dry Chemical, Foam

UNUSUAL FIRE AND EXPLOSION HAZARDS

Closed containers may explode when exposed to extreme heat.

Application to hot surfaces requires special precautions.

During emergency conditions overexposure to decomposition products may cause a health hazard. Symptoms may not be immediately apparent. Obtain medical attention.

SPECIAL FIRE FIGHTING PROCEDURES

Full protective equipment including self-contained breathing apparatus should be used.

Water spray may be ineffective. If water is used, fog nozzles are preferable. Water may be used to cool closed containers to prevent pressure build-up and possible auto ignition or explosion when exposed to extreme heat.

Section 6 -- Accidental Release Measures

STEPS TO BE TAKEN IN CASE MATERIAL IS RELEASED OR SPILLED

Remove all sources of ignition. Ventilate the area.

Remove with inert absorbent.

Section 7 -- Handling and Storage

STORAGE CATEGORY

DOL Storage Class IB

PRECAUTIONS TO BE TAKEN IN HANDLING AND STORAGE

Contents are EXTREMELY FLAMMABLE. Keep away from heat, sparks, and open flame. Vapors will accumulate readily and may ignite explosively.

During use and until all vapors are gone: Keep area ventilated - Do not smoke - Extinguish all flames, pilot lights, and heaters - Turn off stoves, electric tools and appliances, and any other sources of ignition.

Consult NFPA Code. Use approved Bonding and Grounding procedures.

Keep container closed when not in use. Transfer only to approved containers with complete and appropriate labeling. Do not take internally.

Keep out of the reach of children.

Section 8 -- Exposure Controls/Personal Protection

PRECAUTIONS TO BE TAKEN IN USE

NO PERSON SHOULD USE THIS PRODUCT, OR BE IN THE AREA WHERE IT IS BEING

USED, IF THEY HAVE CHRONIC (LONG-TERM) LUNG OR BREATHING PROBLEMS OR IF

THEY EVER HAD A REACTION TO ISOCYANATES.

Certain colors contain Lead (see PRODUCT LABEL). Before initial use, consult OSHA's 'Standard for Occupational Exposure to Lead' (29 CFR 1910.1025.)

Use only with adequate ventilation. Avoid contact with skin and eyes.

Avoid breathing vapor and spray mist. Wash hands after using.

This coating may contain materials classified as nuisance particulates (listed "as Dust" in Section 2) which may be present at hazardous levels only during sanding or abrading of the dried film. If no specific dusts are listed in Section 2, the applicable limits for nuisance dusts are ACGIH

TLV 10 mg/m3 (total dust), 3 mg/m3 (respirable fraction), OSHA PEL 15 mg/m3 (total dust), 5 mg/m3 (respirable fraction).

VENTILATION: Local exhaust preferable. General exhaust acceptable if the exposure to materials in Section 2 is maintained below applicable exposure limits.

Refer to OSHA Standards 1910.94, 1910.107, 1910.108.

RESPIRATORY PROTECTION

Where overspray is present, a positive pressure air supplied respirator

(TC19C NIOSH/MSHA approved) should be worn. If unavailable, a properly fitted organic vapor/particulate respirator approved by NIOSH/MSHA for protection against materials in Section 2 may be effective. Follow respirator manufacturer's directions for use. Wear the respirator for the whole time of spraying and until all vapors and mists are gone. NO PERSONS

SHOULD BE ALLOWED IN THE AREA WHERE THIS PRODUCT IS BEING USED UNLESS EQUIPPED WITH THE SAME RESPIRATOR PROTECTION RECOMMENDED FOR THE PAINTERS.

When sanding, wire brushing, abrading, burning or welding the dried film, wear a particulate respirator approved by NIOSH/MSHA for protection against non-volatile materials in Section 2.

PROTECTIVE GLOVES

To prevent skin contact, wear gloves which are recommended by glove supplier for protection against materials in Section 2.

EYE PROTECTION

Wear safety spectacles with unperforated side shields.

OTHER PROTECTIVE EQUIPMENT

Use barrier cream on exposed skin.

OTHER PRECAUTIONS

Certain colors contain Lead (see PRODUCT LABEL). Do not apply on toys and other children's articles, furniture, or any interior surface of a dwelling or facility which may be occupied or used by children. Do not apply on any exterior surface of dwelling units, such as window sills, porches, stairs, or railings to which children may be commonly exposed.

This product must be mixed with other components before use. Before opening the packages, READ AND FOLLOW WARNING LABELS ON ALL COMPONENTS.

Intentional misuse by deliberately concentrating and inhaling the contents can be harmful or fatal.

Section 9 -- Physical and Chemical Properties

PRODUCT WEIGHT 8-10 lb/gal 960-1200 g/l

SPECIFIC GRAVITY 0.96-1.20

BOILING POINT 132 - 395 °F 55 - 201 °C

MELTING POINT Not Available

VOLATILE VOLUME 54-65 % EVAPORATION RATE Slower than ether

VAPOR DENSITY Heavier than air

SOLUBILITY IN WATER N.A.

VOLATILE ORGANIC COMPOUNDS (VOC Theoretical - As Packaged)

3.5-4.4 lb/gal 420-520 g/l Less Water and Federally Exempt Solvents

3.2-4.0 lb/gal 380-470 g/l Emitted VOC

Section 10 -- Stability and Reactivity

STABILITY -- Stable

CONDITIONS TO AVOID: None known.

INCOMPATIBILITY:

Metallics may contain aluminum. Contamination with Water, Acids, or

Alkalis can cause evolution of hydrogen, which may result in dangerously increased pressure in closed containers.

HAZARDOUS DECOMPOSITION PRODUCTS

By fire: Carbon Dioxide, Carbon Monoxide, Oxides of Metals in Section 2

HAZARDOUS POLYMERIZATION

Will not occur

Section 11 -- Toxicological Information

CHRONIC HEALTH HAZARDS

Certain colors contain Lead or Chromium (see PRODUCT LABEL).

Chronic overexposure to Lead may result in damage to the blood-forming, nervous, urinary, and reproductive systems (including embryotoxic effects).

Symptoms include abdominal discomfort or pain, constipation, loss of appetite, metallic taste, nausea, insomnia, nervous irritability, weakness, muscle and joint pains, headache and dizziness.

Chromates are listed by IARC and NTP. Although studies have associated exposure to Chromium VI compounds with an increased risk of respiratory cancer, available evidence indicates that Lead Chromate (Chrome Yellow,

Molybdate Orange) DOES NOT present this hazard.

Ethylbenzene is classified by IARC as possibly carcinogenic to humans (2B) based on inadequate evidence in humans and sufficient evidence in laboratory animals. Lifetime inhalation exposure of rats and mice to high

ethylbenzene concentrations resulted in increases in certain types of cancer, including kidney tumors in rats and lung and liver tumors in mice.

These effects were not observed in animals exposed to lower concentrations.

There is no evidence that ethylbenzene causes cancer in humans.

Carbon Black is classified by IARC as possibly carcinogenic to humans (group 2B) based on experimental animal data, however, there is insufficient evidence in humans for its carcinogenicity.

Limited evidence exists linking certain Nickel compounds to cancer in animals and possibly humans, however no direct evidence exists that Nickel

Antimony Titanate is carcinogenic.

Prolonged overexposure to solvent ingredients in Section 2 may cause adverse effects to the liver, urinary, blood forming, cardiovascular and reproductive systems.

Persons sensitive to isocyanates will experience increased allergic reaction on repeated exposure.

Rats exposed to titanium dioxide dust at 250 mg./m3 developed lung cancer, however, such exposure levels are not attainable in the workplace.

Reports have associated repeated and prolonged overexposure to solvents with permanent brain and nervous system damage.

TOXICOLOGY DATA CAS No. Ingredient Name

64742-88-7 Mineral Spirits

LC50 RAT 4HR Not Available

LD50 RAT Not Available

108-88-3 Toluene

LC50 RAT 4HR 4000 ppm

LD50 RAT 5000 mg/kg

100-41-4 Ethylbenzene

LC50 RAT 4HR Not Available

LD50 RAT 3500 mg/kg

1330-20-7 Xylene

LC50 RAT 4HR 5000 ppm

LD50 RAT 4300 mg/kg

111-76-2 2-Butoxyethanol

LC50 RAT 4HR Not Available

LD50 RAT 470 mg/kg

67-64-1 Acetone

LC50 RAT 4HR Not Available

LD50 RAT 5800 mg/kg

107-87-9 Methyl n-Propyl Ketone

LC50 RAT 4HR Not Available

LD50 RAT 1600 mg/kg

123-86-4 n-Butyl Acetate

LC50 RAT 4HR 2000 ppm

LD50 RAT 13100 mg/kg

112-07-2 2-Butoxyethyl Acetate

LC50 RAT 4HR Not Available

LD50 RAT 2400 mg/kg

Proprietary Coated Mica

LC50 RAT 4HR Not Available

LD50 RAT Not Available

13463-67-7 Titanium Dioxide

LC50 RAT 4HR Not Available

LD50 RAT Not Available

1333-86-4 Carbon Black

LC50 RAT 4HR Not Available

LD50 RAT Not Available

1344-37-2 Lead Chromate

LC50 RAT 4HR Not Available

LD50 RAT Not Available

8007-18-9 Nickel Antimony Titanate

LC50 RAT 4HR Not Available

LD50 RAT 499.9 mg/kg

12656-85-8 Molybdate Orange

LC50 RAT 4HR Not Available

LD50 RAT Not Available

Section 12 -- Ecological Information

ECOTOXICOLOGICAL INFORMATION

No data available.

Section 13 -- Disposal Considerations

WASTE DISPOSAL METHOD

Waste from this product may be hazardous as defined under the Resource Conservation and Recovery Act (RCRA) 40 CFR 261.

Waste must be tested for ignitability and extractability to determine the applicable EPA hazardous waste numbers.

Incinerate in approved facility. Do not incinerate closed container.

Dispose of in accordance with Federal, State/Provincial, and Local regulations regarding pollution.

Section 14 -- Transport Information

No data available.

Section 15 -- Regulatory Information

SARA 313 (40 CFR 372.65C) SUPPLIER NOTIFICATION CAS No. CHEMICAL/COMPOUND % by WT % Element

108-88-3 Toluene max 2

100-41-4 Ethylbenzene max 5

1330-20-7 Xylene max 30

Chromium Compound max 17 2.0

Nickel Compound max 10 0.9

Antimony Compound max 10 0.2

Lead Compound max 17 9.6

Glycol Ethers max 4

CALIFORNIA PROPOSITION 65

WARNING: This product contains chemicals known to the State of California to cause cancer and birth defects or other reproductive harm.

TSCA CERTIFICATION

All chemicals in this product are listed, or are exempt from listing, on the TSCA Inventory.

Section 16 -- Other Information

This product has been classified in accordance with the hazard criteria of the Canadian Controlled Products Regulations (CPR) and the MSDS contains all of the information required by the CPR.

The above information pertains to this product as currently formulated, and is based on the information available at this time. Addition of reducers or other additives to this product may substantially alter the composition and hazards of the product. Since conditions of use are outside our control, we make no warranties, express or implied, and assume no liability in connection with any use of this information.

5 STAR MATERIAL SAFETY DATA SHEET

MSDS No: 301.0358737-002.007

#5700 Economy Gun Wash Thinner

1. CHEMICAL PRODUCT AND COMPANY IDENTIFICATION

Material Identity

Product Name: #5700 Economy Gun Wash Thinner

SAP Material No.: 2289123 000 00B

General or Generic ID: SOLVENT BLEND

Company

ABI/Autobody Brands International a division of IAMG/International Autobody Marketing Group

9419 E. San Salvador Dr. Suite 104

Scottsdale, AZ 85258

Information phone: 1-87-REFINISH

Emergency Telephone Number: 1-800-424-9300 CHEMTREC (24hrs/day)

2. COMPOSITION/INFORMATION ON INGREDIENTS

Ingredient(s) CAS Number % (by weight)

-------------------------------------------- ------------- -------------

TOLUENE 108-88-3 53.0 - 53.0

METHANOL 67-56-1 20.0 - 20.0

ALIPHATIC HYDROCARBON 64742-89-8 11.0 – 15.0

ACETONE 67-64-1 10.0 - 14.0

2, 2-DIMETHOXYPROPANE 77-76-9 1.0 – 3.6

3. HAZARDS IDENTIFICATION

Potential Health Effects

Eyes Can cause eye irritation. Symptoms include stinging, tearing, redness, and swelling of eyes.

Skin May cause mild skin irritation. Prolonged or repeated contact may dry the skin.

Symptoms may include redness, burning, drying and cracking of skin, and skin burns.

Passage of this material into the body through the skin is possible, and may add to toxic effects from breathing or swallowing.

Swallowing

Swallowing this material may be harmful. This material can get into the lungs during swallowing or vomiting. This results in lung inflammation and other lung injury.

Inhalation

Breathing of vapor or mist is possible. Breathing small amounts of this material during normal handling is not likely to cause harmful effects. Breathing large

5700 Page 2 of 9 amounts may be harmful. Symptoms usually occur at air concentrations higher than the recommended exposure limits (See Section 8).

Symptoms of Exposure

Signs and symptoms of exposure to this material through breathing, swallowing, and/or passage of the material through the skin may include: metallic taste, mouth and throat irritation (soreness, dry or scratchy feeling, cough), stomach or intestinal upset (nausea, vomiting, diarrhea), irritation (nose, throat, airways), central nervous system excitation (giddiness, liveliness, light-headed feeling) followed by central nervous system depression (dizziness, drowsiness, weakness, fatigue, nausea, headache, unconsciousness) and other central nervous system effects, temporary changes in mood and behavior, leg cramps, muscle weakness, pain in the abdomen and lower back, blurred vision, shortness of breath, loss of coordination, confusion, irregular heartbeat, cyanosis (causes blue coloring of the skin and nails from lack of oxygen), high blood sugar, visual impairment (including blindness), coma, and death.

Target Organ Effects

This material (or a component) shortens the time of onset or worsens the liver and kidney damage induced by other chemicals. Exposure to lethal concentrations of methanol has been shown to cause damage to organs including liver, kidneys, pancreas, heart, lungs and brain. Although this rarely occurs, survivors of severe intoxication may suffer from permanent neurological damage. Prolonged intentional toluene abuse may lead to damage to many organ systems having effects on: central and peripheral nervous systems, vision, hearing, liver, kidneys, heart and blood.

Such abuse has been associated with brain damage characterized by disturbances in gait, personality changes and loss of memory. Comparable central nervous system effects have not been shown to result from occupational exposure to toluene.

Prolonged intentional toluene abuse may lead to hearing loss progressing to deafness. In addition, while noise is known to cause hearing loss in humans, it has been suggested that workers exposed to organic solvents, including toluene, along with noise may suffer greater hearing loss than would be expected from exposure to noise alone. Overexposure to this material (or its components) has been suggested as a cause of the following effects in laboratory animals: mild, reversible kidney effects, blood abnormalities, liver abnormalities, respiratory tract damage (nose, throat and airways), effects on hearing, central nervous system damage. Overexposure to this material (or its components) has been suggested as a cause of the following effects in humans: kidney damage, visual impairment.

Developmental Information

Toluene may be harmful to the human fetus based on positive test results with laboratory animals. Case studies show that prolonged intentional abuse of toluene during pregnancy can cause birth defects in humans. Methanol has caused birth defects in laboratory animals, but only when inhaled at extremely high vapor concentrations. The relevance of this finding to humans is uncertain.

Cancer Information

Based on the available information, this material cannot be classified with regard to carcinogenicity. This material is not listed as a carcinogen by the

International Agency for Research on Cancer, the National Toxicology Program, or the Occupational Safety and Health Administration.

Other Health Effects

No data

5700 Page 3 of 9

Primary Route(s) of Entry Inhalation, Skin absorption, Skin contact, Eye contact, Ingestion.

4. FIRST AID MEASURES

Eyes

If symptoms develop, immediately move individual away from exposure and into fresh air. Flush eyes gently with water for at least 15 minutes while holding eyelids apart; seek immediate medical attention.

Skin

Remove contaminated clothing. Wash exposed area with soap and water. If symptoms persist, seek medical attention. Launder clothing before reuse.

Swallowing

Seek medical attention. If individual is drowsy or unconscious, do not give anything by mouth; place individual on the left side with the head down. Contact a physician, medical facility, or poison control center for advice about whether to induce vomiting. If possible, do not leave individual unattended.

Inhalation If symptoms develop, move individual away from exposure and into fresh air. If symptoms persist, seek medical attention. If breathing is difficult, administer oxygen. Keep person warm and quiet; seek immediate medical attention.

Note to Physicians

Inhalation of high concentrations of this material, as could occur in enclosed spaces or during deliberate abuse, may be associated with cardiac arrhythmias.

Sympathomimetic drugs may initiate cardiac arrhythmias in persons exposed to this material. This product contains methanol which can cause intoxication and central nervous system depression. Methanol is metabolized to formic acid and formaldehyde.

These metabolites can cause metabolic acidosis, visual disturbances and blindness.

Since metabolism is required for these toxic symptoms, their onset may be delayed from 6 to 30 hours following ingestion. Ethanol competes for the same metabolic pathway and has been used to prevent methanol metabolism. Ethanol administration is indicated in symptomatic patients or at blood methanol concentrations above 20 ug/dl. Methanol is effectively removed by hemodialysis. Fomepizole (4- methylpyrazole) is an effective antagonist of alcohol dehydrogenase, and as such, may be used as an antidote in the treatment of ethylene glycol, diethylene glycol and methanol poisoning. This material is an aspiration hazard. Potential danger from aspiration must be weighed against possible oral toxicity (See Section 3 - Swallowing) when deciding whether to induce vomiting. This material (or a component) has produced hyperglycemia and ketosis following substantial ingestion.

Preexisting disorders of the following organs (or organ systems) may be aggravated by exposure to this material: skin, lung (for example, asthma-like conditions), liver, kidney, central nervous system, pancreas, heart, blood-forming system, male reproductive system, auditory system. Exposure to this material may aggravate any preexisting condition sensitive to a decrease in available oxygen, such as chronic lung disease, coronary artery disease or anemia’s. Individuals with preexisting heart disorders may be more susceptible to arrhythmias (irregular heartbeats) if exposed to high concentrations of this material.

5700 Page 4 of 9

5. FIRE FIGHTING MEASURES

Flash Point

10.0 - 19.0 F (-12.2 - -7.2 C) TCC

Explosive Limit (for component) Lower 1.2 Upper 36.0 %

Autoignition Temperature

No data

Hazardous Products of Combustion May form: carbon dioxide and carbon monoxide, various hydrocarbons.

Fire and Explosion Hazards

Material is highly volatile and readily gives off vapors which may travel along the ground or be moved by ventilation and ignited by pilot lights, other flames, sparks, heaters, smoking, electric motors, static discharge, or other ignition sources at locations distant from material handling point. Never use welding or cutting torch on or near drum (even empty) because product (even just residue) can ignite explosively.

Extinguishing Media regular foam, water fog, carbon dioxide, dry chemical.

Fire Fighting Instructions

Wear a self-contained breathing apparatus with a full face piece operated in the positive pressure demand mode with appropriate turn-out gear and chemical resistant personal protective equipment. Refer to the personal protective equipment section of this MSDS.

NFPA Rating

Health - 2, Flammability - 3, Reactivity - 0

6. ACCIDENTAL RELEASE MEASURES

Small Spill

Eliminate all sources of ignition such as flares, flames (including pilot lights), and electrical sparks. Absorb liquid on vermiculite, floor absorbent or other absorbent material. Persons not wearing proper personal protective equipment should be excluded from area of spill.

Large Spill

Prevent run-off to sewers, streams or other bodies of water. If run-off occurs, notify proper authorities as required, that a spill has occurred. Persons not wearing protective equipment should be excluded from area of spill until clean-up has been completed. Eliminate all ignition sources (flares, flames including pilot lights, electrical sparks).

7. HANDLING AND STORAGE

Handling

Containers of this material may be hazardous when emptied. Since emptied containers retain product residues (vapor, liquid, and/or solid), all hazard precautions given in the data sheet must be observed. All five-gallon pails and larger metal containers, including tank cars and tank trucks, should be grounded and/or bonded when material is transferred. Precautions during use: avoid prolonged or frequently repeated skin contact with this material. Skin contact can be minimized by wearing impervious protective gloves. As with all products of this nature, good

5700 Page 5 of 9 personal hygiene is essential. Hands and other exposed areas should be washed thoroughly with soap and water after contact, especially before eating and/or smoking. Regular laundering of contaminated clothing is essential to reduce indirect skin contact with this material. Hydrocarbon solvents are basically nonconductors of electricity and can become electrostatically charged during mixing, filtering or pumping at high flow rates. If this charge reaches a sufficiently high level, sparks can form that may ignite the vapors or mists from process equipment operating at elevated temperature and pressure, or sudden ingress of air into vacuum equipment, may result in ignitions without the presence of obvious ignition sources. Published “auto ignition” or “ignition” temperature values cannot be treated as safe operating temperatures in chemical processes without analysis of the actual process conditions. Any use of this product in elevated temperature processes should be thoroughly evaluated to establish and maintain safe operating conditions.

Storage

Do not store near extreme heat, open flame, or sources of ignition.

8. EXPOSURE CONTROLS/PERSONAL PROTECTION

Eye Protection

Chemical splash goggles in compliance with OSHS regulations are advised; however,

OSHA regulations also permit other type safety glasses. Consult your safety representative.

Skin Protection

Wear resistant gloves (consult your safety equipment supplier). To prevent repeated or prolonged skin contact, wear impervious clothing and boots.

Respiratory Protections

If workplace exposure limit(s) of product or any component is exceeded (see exposure guidelines), a NIOSH/MSHA approved air supplied respirator is advised in absence of proper environmental control. OSHA regulations also permit other

NIOSH/MSHA respirators (negative pressure type) under specified conditions (see your industrial hygienist). Engineering or administrative controls should be implemented to reduce exposure.

Engineering Controls

Provide sufficient mechanical (general and/or local exhaust) ventilation to maintain exposure below TLV(s).

Exposure Guidelines

Component

----------

TOLUENE (108-88-3)

OSHA PEL 200.000 ppm - TWA

OSHA PEL 300.000 ppm - Ceiling

OSHA VPEL 100.000 ppm - TWA

OSHA VPEL 150.000 ppm - STEL

ACGIH TLV 50.000 ppm – TWA (Skin)

ACGIH TLV 150.000 ppm – STEL (Skin)

METHANOL (67-56-1)

OSHA PEL 200.000 ppm - TWA

OSHA VPEL 200.000 ppm - TWA (Skin)

OSHA VPEL 250.000 ppm - STEL (Skin)

5700 Page 6 of 9

ACGIH TLV 200.000 ppm - TWA (Skin)

ACGIH TLV 250.000 ppm - STEL (Skin)

ALIPHATIC HYDROCARBON (64742-89-8)

OSHA VPEL 300.000 ppm - TWA

OSHA VPEL 400.000 ppm - STEL

ACGIH TLV 300.000 ppm – TWA

ACETONE (67-64-1)

OSHA PEL 1000.000 ppm - TWA

OSHA VPEL 750.000 ppm - TWA

OSHA VPEL 1000.000 ppm - STEL

ACGIH TLV 500.000 ppm - TWA

ACGIH TLV 750.000 ppm - STEL

2,2-DIMETHOXYPROPANE (77-76-9)

No exposure limits established

9. PHYSICAL AND CHEMICAL PROPERTIES

Boiling Point

(for component) 133.0 F (56.1 C)

Vapor Pressure

(for blend) 73.00 mmHg @ 68.00 F

(CA-SCAQMD) 49.0 mmHg @ 68.00 F

Specific Vapor Density

> 1.000 @ AIR=1

Specific Gravity

.823 @ 68.00 F

Liquid Density

6.69850 lbs/gal @ 68.00 F

.823 kg/l @ 20.00 C

Percent Volatiles

No Data

Volatile Organic Compounds (VOC)

725.500 g/l (CA-SCAQMD)

6.850 lbs/gal (for blend)

Evaporation Rate

SLOWER THAN ETHYL ETHER

Appearance

CLEAR AND PARTICLE FREE

State

LIQUID

Physical Form

HOMOGENEOUS SOLUTION

Color

No Data

5700 Page 7 of 9

Odor

No Data

pH

Not Applicable

10. STABILITY AND REACTIVITY

Hazardous Polymerization

Product will not undergo hazardous polymerization.

Hazardous Decomposition may form: carbon dioxide and carbon monoxide, various hydrocarbons.

Chemical Stability: Stable.

Incompatibility

Avoid contact with: acids, amines, reactive metals such as aluminum and magnesium, strong alkalis, strong oxidizing agents.

11. TOXICOLOGICAL INFORMATION

No data

12. ECOLOGICAL INFORMATION

No data

13. DISPOSAL CONSIDERATION

Waste Management Information

Dispose of in accordance with all applicable local, state and federal regulations.

Do not discharge effluent containing this product into lakes, streams, ponds or estuaries, oceans, or other waters unless in accordance with the requirements of a

National Pollutant Discharge Elimination System (NPDES) permit and the permitting authority has been notified in writing prior to discharge. Do not discharge effluent containing this product to sewer systems without previously notifying the local sewage treatment plant authority. For guidance, contact your State Water Board or Regional Office of the EPA.

14. TRANSPORT INFORMATION

DOT Information - 49 CFR 172.101

DOT Description:

PAINT RELATED MATERIALS,3,UN1263,II

Container/Mode:

55 GAL DRUM/TRUCK PACKAGE

NOS Component:

Not applicable

RQ (Reportable Quantity) - 49 CFR 172.101

Product Quantity (lbs) Component

---------------------- --------------------------------------------------

1888 TOLUENE

25615 METHANOL

41179 ACETONE

5700 Page 8 of 9

Other Transportation Information

The Transport Information may vary with the container and mode of shipment.

15. REGULATORY INFORMATION

US Federal Regulations

TSCA (Toxic Substances Control Act) Status

TSCA (UNITED STATES) The intentional ingredients of this product are

listed.

CERCLA RQ - 40 CFR 302.4(a)

Component RQ (lbs)

---------------------------------------- ---------

TOLUENE 1000

METHYL ALCOHOL 5000

ACETONE 5000

CERCLA RQ - 40 CFR 302.4(b)

Materials without a “listed” RQ may be reportable as an “unlisted hazardous substance”. See 40 CFR 302.5 (b)

SARA 302 Components - 40 CFR 355 Appendix A

None

Section 311/312 Hazard Class - 40 CFR 370.2

Immediate(X) Delayed(X) Fire(X) Reactive( ) Sudden

Release of Pressure( )

SARA 313 Components - 40 CFR 372.65

Section 313 Component(s) CAS Number %

---------------------------------------- ------------- ------

TOLUENE 100-41-4 52.96

METHANOL 67-56-1 19.51

OSHA Process Safety Management 29 CFR 1910

None listed

EPA Accidental Release Prevention 40 CFR 68

None listed

International Regulations

Inventory Status

Not determined

State and Local Regulations

California Proposition 65

The following statement is made in order to comply with the California Safe

Drinking Water and Toxic Enforcement Act of 1986: This product contains the following substance(s) known to the state of California to cause cancer.

BENZENE

ACETALDEHYDE

FORMALDEHYDE (GAS)

The following statement is made in order to comply with the California Safe

Drinking Water and Toxic Enforcement Act of 1986: This product contains the

5700 Page 9 of 9 following substance(s) known to the state of California to cause reproductive harm.

TOLUENE

BENZENE

New Jersey RTK Label Information

TOLUENE 108-88-3

METHYL ALCOHOL 67-56-1

NAPHTHA, SOLVENT 64742-89-8

ACETONE 67-64-1

Pennsylvania RTK Label Information

BENZENE, METHYL- 108-88-3

METHANOL 67-56-1

ALIPHATIC HYDROCARBON 64742-89-8

2-PROPANONE 67-64-1

16. OTHER INFORMATION

The information accumulated herein is believed to be accurate but is not warranted to be whether originating with the company or not. Recipients are advised to confirm in advance of need that the information is current, applicable, and suitable to their circumstances.

MATERIAL SAFETY DATA SHEET &

EMERGENCY RESPONSE INFORMATION

Revised: October 23, 2002

Manufacturer: Animal Motor Works, Inc.

Address: 5951 Riverside Drive

Port Orange, FL 32127

Emergency Response

Telephone Number: (800) 451-8346

SECTION I – PRODUCT IDENTIFICATION

Product Name: Rocket Motor Reload Kits

Synonyms: Black Bear Propellant™, Blue Baboon Propellant™, Green

Gorilla Propellant™, Greyhound Propellant™, Purple Parrot

Propellant™, Red Rhino Propellant™, Skidmark Propellant™,

Super Tiger Propellant™, White Wolf Propellant™

Proper Shipping Name: Articles, explosives, n. o. s.

1.4C, UN0351, PG II (DOT-E 10996)

SECTION II – HAZARDOUS INGREDIENTS

These articles contain propellant and delay charge modules which consist primarily of ammonium perchlorate (NH4ClO4) dispersed in synthetic rubber.

SECTION III – PHYSICAL DATA

Boiling Point Range: Decomposes

Specific Gravity: Propellant ranges from 1.35 to 2.25

Appearance: Silver static shielding bags containing cylindrical segments and o-rings

Odor: None

Physical State: Solid

SECTION IV – FIRE AND EXPLOSION HAZARD DATA

Autoignition Temperature: 280°C

Flammability: Flammable

Extinguishing Media: Water only

Special Fire Procedures: Extinguish with water only

Protect against toxic fumes

Unusual Fire Hazard: Burning propellant gives off hydrogen chloride gas.

Unusual Explosion Hazard: None anticipated

SECTION V – HEALTH HAZARD DATA

Effects of Overexposure:

Acute: None known

Chronic: None Known

Overexposure:

Eyes: Ammonium perchlorate is a mild irritant to the skin, eyes, mucous membranes and the digestive tract.

Skin: Ammonium perchlorate is a mild irritant to the skin, eyes, mucous membranes and the digestive tract.

Inhalation: No information available

Ingestion: Ammonium perchlorate is a mild irritant to the skin, eyes, mucous membranes and the digestive tract.

SECTION VI – EMERGENCY FIRST AID PROCEDURES

Ingestion: If swallowed, induce vomiting, Call a physician.

Inhalation: Avoid breathing exhaust fumes.

Skin Contact: For mild burns, use a first aid burn ointment.

For severe burns, see a physician immediately.

If loose ammonium perchlorate contacts skin, flush with plenty of water.

Eye Contact: Immediately flush eyes with plenty of water for at least 15 minutes. Call a physician.

Note to physician: Chemical of exposure is ammonium perchlorate, a mild gastric irritant.

SECTION VII – REACTIVITY DATA

Conditions to Avoid: Heat (propellant auto-ignites at 280°C)

Incompatibility: Acids

Hazardous Products

Of Decomposition: Oxides of carbon, hydrogen chloride gas

SECTION VIII – SPILL OR LEAK PROCEDURES

Spills: Replace articles in packaging and boxes and seal securely.

Waste Disposal Method: Pack reload kit firmly in hole in ground. Ignite reload kit electrically from a safe distance and wait 5 minutes before approaching. Dispose of spent reload components in inert trash.

SECTION IX – SPECIAL PROTECTION INFORMATION

Ventilation Requirements: None. Do not use reload kits indoors.

Special Personal Protective Equipment

Respiratory: None. Avoid breathing exhaust fumes.

Other Handling and

Storage Requirements: Store reload kits away from sources of heat and highly flammable materials.

When handling components inside the protective packaging, wear skin protection, such as latex or nitrile gloves.

8.8 Our only environmental concern is starting a grass fire while launching our rocket which is why we only launch on cemented or graveled areas.

9. Payload Criteria

9.1. System level design review

Proposed GPS system

The GPS Flight GPS system will be used as our rocket locator as well as another set of data that we can compare the altimeters with. It will be used in the full sized rocket and possibly the scaled down version as well.

HD video camera

The Kodak Zi6 HD Video Camera is our current choice and will be used as our reference baseline for comparing data. It will be mounted in the full sized rocket.

Miniature camera

The BoosterVision MiniGear Cam video camera will be used as a substitute for the Zi6 in the scaled down rocket because of weight and size issues. One of our mentors already has this equipment and has agreed to lend it to us. It should provide accurate video data at the lower altitudes we plan to fly our test flights.

Barometric altimeter

The PerfectFlight Mini Alt/WD logging dual event altimeter will be used as our main altimeter and deployment device. It will be used in the full sized rocket as well as the scale version.

Accelerometer based altimeter

The Pico Altimeter PICO-AA2 will be used as our backup altimeter in the full sized rocket as well as another set of data. It will not be used in the scale version for simplicity.

9.2 The payload subsystems are the altimeters, the GPS systems, and the camera systems.

9.3 When we place multiple altimeters in our TARC rockets we have found up to a 30 foot difference in altitude in the same payload bay on the same flight. Because of this previous experience from TARC, we wish to quantify our accuracy level findings.

10. Payload concept features and definition

10.1 Our payload is an extremely precise and creative way to test altimeter accuracy.

10.2 It is significant because of personal experience with inaccurate altimeters used in the Team America Rocketry Challenge. We are interested in determining the level of accuracy these altimeters actually have at many different altitudes.

10.3 It is a suitable challenge for everyone on the team to build and fly the rocket, and will be a difficult challenge for the payload team to analyze the data and present it in a usable and detailed final report.

11. Science value

11.1The objective of our payload is to be able to digitally record a launch to be able determine the rocket’s altitude and to then compare the camera data with the altimeters to determine the altimeters accuracy.

11.2 For our payload to be successful we need to have the camera to be able to film a launch, and for the altimeters and GPS to be able to read an altitude.

12. Safety and environment

12.1 Our safety officer is Trenton Tulloss

12.2 We have given failure modes information in Vehicle Safety and Environment

12.3 We have given personnel hazards information in Vehicle Safety and Environment

12.4 We have no environmental concerns

13. Activity Plan

13.1 Budget for the 2009 N.A.S.A. Student Launch Initiative

1.  Rocket Equipment, including both consumables and non-consumable materials. Total estimate: 				$2900

2.Round trip airfare for nine people: 		$6270

3. Hotel cost, four dbl. rooms, five nights:       	$1800

4. Rental car cost one twelve passenger van,

six days	$750

5. Fuel:						$200

6. Food cost meals two hundred thirty

dollars per day:					$1620

7. Last minute incidentals cost: 			$400

8. Total cost:						$13,910

Our updated schedule:

We completed an outreach event on 12/4/08 in which we introduced approximately 40 teen students to the SLI program. In addition, we handed out printed contact information to 14 individuals. The event was the Third Annual Cherry Creek Association for Gifted and Talented (ChCAGT) Math and Science Career Fair at Cherry Creek High School in Denver.

COSROCS is having a rocketry class with SLI help and promotion of NASA this Saturday, Dec. 6th.  During the first half of all of our classes (1:00 – 2:30), we teach a subject relating to model rocketry. Last time, we talked about the history of rocketry.  This month we are discussing the agencies that govern model rocketry, go over definitions of rocketeers and model rocketry skill levels, and talk about the different types of model rockets.

The second half of the class (2:30 – 4:00) we have the kids work on their model rockets. Most of the kids have never built a model rocket before. Some of the kids are also 4-H members taking model rocketry as their 4-H project for the  year.  Most of the kids participating in the class range in ages from 12- to 14-years old.

We will document the number of SLI outreach contacts we make.

Additional team member.

Nathaniel has rejoined the team in order to provide web site support and help with data analysis for the payload team.

Nate is a freshman at the Vanguard School, and has participated in TARC for two years. In 7th grade, Nathaniel scored the highest grade in the Colorado Student Assessment Program math portion, in the school ranked highest in Colorado. He is an avid music fan, enjoys playing guitar, and was on Vanguard’s homecoming court this year. He also enjoys Latin, physics, and chemistry. Nate often works as a caregiver for his grandparents.